## Slide 1: DATA COMMUNICATION
Data Communications concerns the transmission of digital messages to devices external to the message source
"External" devices are generally thought of as being independently powered circuitry that exists beyond the chassis of a computer or other digital message source.
As a rule, the maximum permissible transmission rate of a message is directly proportional to signal power, and inversely proportional to channel noise.

## Slide 2: DATA COMMUNICATION
It is the aim of any communications system to provide the highest possible transmission rate at the lowest possible power and with the least possible noise

## Slide 3: Communications Channels
A communications channel is a pathway over which information can be conveyed
It may be defined by a physical wire that connects communicating devices, or by a radio, laser, or other radiated energy source that has no obvious physical presence
Information sent through a communications channel has a source from which the information originates, and a destination to which the information is delivered
Although information originates from a single source, there may be more than one destination, depending upon how many receive stations are linked to the channel and how much energy the transmitted signal possesses

## Slide 4: Communications Channels
In a digital communications channel, the information is represented by individual data bits, which may be encapsulated into multi-bit message units.
A byte, which consists of eight bits, is an example of a message unit that may be conveyed through a digital communications channel
A collection of bytes may itself be grouped into a frame or other higher-level message unit
Such multiple levels of encapsulation facilitate the handling of messages in a complex data communications network Any communications channel has a direction associated with it

## Slide 6: Communications Channels conti’
The message source is the transmitter, and the destination is the receiver.
A channel whose direction of transmission is unchanging is referred to as a simplex channel.
For example, a radio station is a simplex channel because it always transmits the signal to its listeners and never allows them to transmit back

## Slide 7
A half-duplex channel is a single physical channel in which the direction may be reversed
Messages may flow in two directions, but never at the same time, in a half-duplex system
In a telephone call, one party speaks while the other listens. After a pause, the other party speaks and the first party listens.
Speaking simultaneously results in garbled sound that cannot be understood.

## Slide 8
A full-duplex channel allows simultaneous message exchange in both directions
It really consists of two simplex channels, a forward channel and a reverse channel, linking the same points
The transmission rate of the reverse channel may be slower if it is used only for flow control of the forward channel

## Slide 9: Serial Communications
Most digital messages are vastly longer than just a few bits
Because it is neither practical nor economic to transfer all bits of a long message simultaneously, the message is broken into smaller parts and transmitted sequentially
Bit-serial transmission conveys a message one bit at a time through a channel
Byte-serial transmission conveys eight bits at a time through eight parallel channels.

## Slide 10: Serial Communications conti’
Although the raw transfer rate is eight times faster than in bit-serial transmission, eight channels are needed, and the cost may be as much as eight times higher to transmit the message.
When distances are short, it may nonetheless be both feasible and economic to use parallel channels in return for high data rates
The popular Centronics printer interface is a case where byte-serial transmission is used.

## Slide 11: Serial Communications conti’
As another example, it is common practice to use a 16-bit-wide data bus to transfer data between a microprocessor and memory chips
this provides the equivalent of 16 parallel channels. On the other hand, when communicating with a timesharing system over a modem, only a single channel is available, and bit-serial transmission is required.

## Slide 12: Serial Communications conti’
As another example, it is common practice to use a 16-bit-wide data bus to transfer data between a microprocessor and memory chips
This provides the equivalent of 16 parallel channels. On the other hand, when communicating with a timesharing system over a modem, only a single channel is available, and bit-serial transmission is required
This figure illustrates these ideas:
Each bit represents a part of the message.
The individual bits are then reassembled at the destination to compose the message

## Slide 14: Serial Communications conti’
In general, one channel will pass only one bit at a time.
Thus, bit-serial transmission is necessary in data communications if only a single channel is available.
Bit-serial transmission is normally just called serial transmission and is the chosen communications method in many computer peripherals

## Slide 15: TRANSMISSION MEDIA
The simplest transmission media consists of a pair of conductors
In the case of inter-equipment communication it often takes the form of a flat ribbon cable containing several lines and a common return wire
This cable is extremely susceptible to inductive or capacitive – induced noise signals from neighboring lines
Much better noise immunity is obtained by the use of pairs of wires which are twisted together
When carrying an analogue signal, it is necessary to insert an amplifiers to boost signal every 5 or 6 km.

## Slide 16: Baud Rate
The baud rate refers to the signaling rate at which data is sent through a channel and is measured in electrical transitions per second
In the EIA232 serial interface standard, one signal transition, at most, occurs per bit, and the baud rate and bit rate are identical.
In this case, a rate of 9600 baud corresponds to a transfer of 9,600 data bits per second with a bit period of 104 microseconds (1/9600 sec.)

## Slide 17: Channel efficiency
If two electrical transitions were required for each bit, as is the case in non-return-to-zero coding, then at a rate of 9600 baud, only 4800 bits per second could be conveyed
The channel efficiency is the number of bits of useful information passed through the channel per second
It does not include framing, formatting, and error detecting bits that may be added to the information bits before a message is transmitted, and will always be less than one.

## Slide 19: Data Rate
The data rate of a channel is often specified by its bit rate (often thought erroneously to be the same as baud rate)
However, an equivalent measure channel capacity is bandwidth
In general, the maximum data rate a channel can support is directly proportional to the channel's bandwidth and inversely proportional to the channel's noise level A communications protocol is an agreed-upon convention that defines the order and meaning of bits in a serial transmission
It may also specify a procedure for exchanging messages
A protocol will define how many data bits compose a message unit, the framing and formatting bits, any error-detecting bits that may be added, and other information that governs control of the communications hardware.

## Slide 20
Channel efficiency is determined by the protocol design rather than by digital hardware considerations.
Note that there is a tradeoff between channel efficiency and reliability - protocols that provide greater immunity to noise by adding error-detecting and -correcting codes must necessarily become less efficient

## Slide 21: Data Rate
Channel efficiency is determined by the protocol design rather than by digital hardware considerations. Note that there is a tradeoff between channel efficiency and reliability - protocols that provide greater immunity to noise by adding error-detecting and -correcting codes must necessarily become less efficient.

## Slide 22: Asynchronous vs. Synchronous Transmission
Serialized data is not generally sent at a uniform rate through a channel
Instead, there is usually a burst of regularly spaced binary data bits followed by a pause, after which the data flow resumes
Packets of binary data are sent in this manner, possibly with variable-length pauses between packets, until the message has been fully transmitted

## Slide 23
In order for the receiving end to know the proper moment to read individual binary bits from the channel, it must know exactly when a packet begins and how much time elapses between bits
When this timing information is known, the receiver is said to be synchronized with the transmitter, and accurate data transfer becomes possible
Failure to remain synchronized throughout a transmission will cause data to be corrupted or lost.

## Slide 24: Asynchronous vs. Synchronous Transmission conti’
Two basic techniques are employed to ensure correct synchronization
In synchronous systems, separate channels are used to transmit data and timing information
The timing channel transmits clock pulses to the receiver
Upon receipt of a clock pulse, the receiver reads the data channel and latches the bit value found on the channel at that moment

## Slide 25: Asynchronous vs. Synchronous Transmission conti’
The data channel is not read again until the next clock pulse arrives.
Because the transmitter originates both the data and the timing pulses, the receiver will read the data channel only when told to do so by the transmitter (via the clock pulse), and synchronization is guaranteed

## Slide 26: Manchester coding
Two methods in which a data signal is self-timed are non-return-to-zero and biphase Manchester coding.
both of these refer to methods for encoding a data stream into an electrical waveform for transmission.

## Slide 27
In asynchronous systems, a separate timing channel is not used
The transmitter and receiver must be preset in advance to an agreed-upon baud rate
A very accurate local oscillator within the receiver will then generate an internal clock signal that is equal to the transmitter's within a fraction of a percent
For the most common serial protocol, data is sent in small packets of 10 or 11 bits, eight of which constitute message information. When the channel is idle, the signal voltage corresponds to a continuous logic '1'

## Slide 28: Data packet
A data packet always begins with a logic '0' (the start bit) to signal the receiver that a transmission is starting
The start bit triggers an internal timer in the receiver that generates the needed clock pulses
Following the start bit, eight bits of message data are sent bit by bit at the agreed upon baud rate The packet is concluded with a parity bit and stop bit
One complete packet is illustrated below:

## Slide 30
The packet length is short in asynchronous systems to minimize the risk that the local oscillators in the receiver and transmitter will drift apart
When high-quality crystal oscillators are used, synchronization can be guaranteed over an 11-bit period. Every time a new packet is sent, the start bit resets the synchronization, so the pause between packets can be arbitrarily long

## Slide 31
Note that the EIA232 standard defines electrical, timing, and mechanical characteristics of a serial interface
However, it does not include the asynchronous serial protocol shown in the previous figure

## Slide 32: Parity and Checksums
Noise and momentary electrical disturbances may cause data to be changed as it passes through a communications channel
A parity bit is a single bit added to a binary data transmission used to indicate if whether the 0's and 1's within that data transmission is an even or odd number. The parity bit is used in parity error checking to find errors that may occur during data transmission. In the picture to the right, is an example of a 8-bit binary number with the ninth digit being the parity bit.
If the receiver fails to detect this, the received message will be incorrect, resulting in possibly serious consequences
As a first line of defense against data errors, they must be detected

## Slide 33
The parity bit, unlike the start and stop bits, is an optional parameter, used in serial communications to determine if the data character being transmitted is correctly received by the remote device
Figure 1. Parity
The parity bit can have one of the following five specifications:
none Specifies that the local system must not create a parity bit for data characters being transmitted. It also indicates that the local system does not check for a parity bit in data received from a remote host
even Specifies that the total number of binary 1s, in a single character, adds up to an even number. If they do not, the parity bit must be a 1 to ensure that the total number of binary 1s is even. For example, if the letter a (binary 1100001) is transmitted under even parity, the sending system adds the number of binary 1s, which in this case is three, and makes the parity bit a 1 to maintain an even number of binary 1s

## Slide 34
If the letter A (binary 1000001) is transmitted under the same circumstances, the parity bit would be a 0, thus keeping the total number of binary 1s an even number
odd Operates under the same guidelines as even parity except that the total number of binary 1s must be an odd number. space Specifies that the parity bit will always be a binary zero. Another term used for space parity is bit filling, which is derived from its use as a filler for seven-bit data being transmitted to a device which can only accept eight bit data

## Slide 35
Such devices see the space parity bit as an additional data bit for the transmitted character
mark Operates under the same guidelines as space parity except that the parity bit is always a binary 1. The mark parity bit acts only as a filler.

## Slide 36
The parity bit for each data packet is computed before the data is transmitted. Below are examples of how a parity bit would be computed using both odd and even parity settings.
Odd parity: Initial value: 1010101 (four 1s)
Parity bit added: 1
Transmitted value: 10101011
Result: Odd parity (five 1s)
Even parity: Initial value: 1010101 (four 1s)
Parity bit added: 0
Transmitted value: 10101010
Result: Even parity (four 1s)
The value of the parity bit depends on the initial parity of the data. For example, the binary value 10000000 has an odd parity

## Slide 37
Therefore, a 0 would be added to keep the parity odd and a 1 would be added to give the value an even parity
While parity checking is a useful way validating data, it is not a foolproof method. For instance, the values 1010 and 1001 have the same parity
Therefore, if the value 1010 is transmitted and 1001 is received, no error will be detected. This means parity checks are not 100% reliable when validating data
Still, it is unlikely that more than one bit will be incorrect in a small packet of data
As long as only one bit is changed, an error will result. Therefore, parity checks are most reliable when using small packet sizes

## Slide 38
If an error can be flagged, it might be possible to request that the faulty packet be resent, or to at least prevent the flawed data from being taken as correct
If sufficient redundant information is sent, one- or two-bit errors may be corrected by hardware within the receiver before the corrupted data ever reaches its destination

## Slide 39
A parity bit is added to a data packet for the purpose of error detection
In the even-parity convention, the value of the parity bit is chosen so that the total number of '1' digits in the combined data plus parity packet is an even number
Upon receipt of the packet, the parity needed for the data is recomputed by local hardware and compared to the parity bit received with the data
If any bit has changed state, the parity will not match, and an error will have been detected. In fact, if an odd number of bits (not just one) have been altered, the parity will not match

## Slide 40
If an even number of bits have been reversed, the parity will match even though an error has occurred
However, a statistical analysis of data communication errors has shown that a single-bit error is much more probable than a multi-bit error in the presence of random noise.
Thus, parity is a reliable method of error detection

## Slide 42
Another approach to error detection involves the computation of a checksum
In this case, the packets that constitute a message are added arithmetically
A checksum number is appended to the packet sequence so that the sum of data plus checksum is zero

## Slide 43
When received, the packet sequence may be added, along with the checksum, by a local microprocessor
If the sum is nonzero, an error has occurred As long as the sum is zero, it is highly unlikely (but not impossible) that any data has been corrupted during transmission

## Slide 45
Errors may not only be detected, but also corrected if additional code is added to a packet sequence
If the error probability is high or if it is not possible to request retransmission, this may be worth doing
However, including error-correcting code in a transmission lowers channel efficiency, and results in a noticeable drop in channel throughput

## Slide 46: Data Compression
If a typical message were statistically analyzed, it would be found that certain characters are used much more frequently than others
By analyzing a message before it is transmitted, short binary codes may be assigned to frequently used characters and longer codes to rarely used characters
In doing so, it is possible to reduce the total number of characters sent without altering the information in the message
Appropriate decoding at the receiver will restore the message to its original form

## Slide 47
This procedure, known as data compression, may result in a 50 percent or greater savings in the amount of data transmitted
Even though time is necessary to analyze the message before it is transmitted, the savings may be great enough so that the total time for compression, transmission, and decompression will still be lower than it would be when sending an uncompressed message

## Slide 48
Some kinds of data will compress much more than others
Data that represents images, for example, will usually compress significantly, perhaps by as much as 80 percent over its original size
Data representing a computer program, on the other hand, may be reduced only by 15 or 20 percent.

## Slide 49
A compression method called Huffman coding is frequently used in data communications, and particularly in fax transmission.
Clearly, most of the image data for a typical business letter represents white paper, and only about 5 percent of the surface represents black ink
It is possible to send a single code that, for example, represents a consecutive string of 1000 white pixels rather than a separate code for each white pixel
Consequently, data compression will significantly reduce the total message length for a faxed business letter
Where the letter made up of randomly distributed black ink covering 50 percent of the white paper surface, data compression would hold no advantages

## Slide 50: Data Encryption
Privacy is a great concern in data communications
Faxed business letters can be intercepted at will through tapped phone lines or intercepted microwave transmissions without the knowledge of the sender or receiver
To increase the security of this and other data communications, including digitized telephone conversations, the binary codes representing data may be scrambled in such a way that unauthorized interception will produce an indecipherable sequence of characters

## Slide 51
Authorized receive stations will be equipped with a decoder that enables the message to be restored. The process of scrambling, transmitting, and descrambling is known as encryption.

## Slide 52
Custom integrated circuits have been designed to perform this task and are available at low cost
In some cases, they will be incorporated into the main circuitry of a data communications device and function without operator knowledge
In other cases, an external circuit is used so that the device, and its encrypting/decrypting technique, may be transported easily

## Slide 53: Data Storage Technology
Normally, we think of communications science as dealing with the contemporaneous exchange of information between distant parties
However, many of the same techniques employed in data communications are also applied to data storage to ensure that the retrieval of information from a storage medium is accurate

## Slide 54
We find, for example, that similar kinds of error-correcting codes used to protect digital telephone transmissions from noise are also used to guarantee correct readback of digital data from compact audio disks, CD-ROMs, and tape backup systems.

## Slide 55: Data Transfer in Digital Circuits
Data is typically grouped into packets that are either 8, 16, or 32 bits long, and passed between temporary holding units called registers
Data within a register is available in parallel because each bit exits the register on a separate conductor
To transfer data from one register to another the output conductors of one register are switched onto a channel of parallel wires referred to as a bus
The input conductors of another register, which is also connected to the bus, capture the information

## Slide 57
Following a data transaction, the content of the source register is reproduced in the destination register
It is important to note that after any digital data transfer, the source and destination registers are equal; the source register is not erased when the data is sent

## Slide 58
The transmit and receive switches shown above are electronic and operate in response to commands from a central control unit.
It is possible that two or more destination registers will be switched on to receive data from a single source.
However, only one source may transmit data onto the bus at any time.
If multiple sources were to attempt transmission simultaneously, an electrical conflict would occur when bits of opposite value are driven onto a single bus conductor.

## Slide 59
Such a condition is referred to as a bus contention
Not only will a bus contention result in the loss of information, but it also may damage the electronic circuitry
As long as all registers in a system are linked to one central control unit, bus contentions should never occur if the circuit has been designed properly
Note that the data buses within a typical microprocessor are funda-mentally half-duplex channels

## Slide 60: Transmission over Short Distances
When the source and destination registers are part of an integrated circuit (within a microprocessor chip, for example), they are extremely close (thousandths of an inch)
Consequently, the bus signals are at very low power levels, may traverse a distance in very little time, and are not very susceptible to external noise and distortion.
This is the ideal environment for digital communications.
However, it is not yet possible to integrate all the necessary circuitry for a computer (i.e., CPU, memory, disk control, video and display drivers, etc.) on a single chip.

## Slide 61
When data is sent off-chip to another integrated circuit, the bus signals must be amplified and conductors extended out of the chip through external pins. Amplifiers may be added to the source register

## Slide 63
Bus signals that exit microprocessor chips and other VLSI circuitry are electrically capable of traversing about one foot of conductor on a printed circuit board, or less if many devices are connected to it
Special buffer circuits may be added to boost the bus signals sufficiently for transmission over several additional feet of conductor length, or for distribution to many other chips (such as memory chips).

## Slide 64: Noise and Electrical Distortion
Because of the very high switching rate and relatively low signal strength found on data, address, and other buses within a computer, direct extension of the buses beyond the confines of the main circuit board or plug-in boards would pose serious problems
First, long runs of electrical conductors, either on printed circuit boards or through cables, act like receiving antennas for electrical noise radiated by motors, switches, and electronic circuits

## Slide 66
Such noise becomes progressively worse as the length increases, and may eventually impose an unacceptable error rate on the bus signals
Just a single bit error in transferring an instruction code from memory to a microprocessor chip may cause an invalid instruction to be introduced into the instruction stream, in turn causing the computer to totally cease operation

## Slide 67
A second problem involves the distortion of electrical signals as they pass through metallic conductors
Signals that start at the source as clean, rectangular pulses may be received as rounded pulses with ringing at the rising and falling edges:

## Slide 69
These effects are properties of transmission through metallic conductors, and become more pronounced as the conductor length increases
To compensate for distortion, signal power must be increased or the transmission rate decreased
Special amplifier circuits are designed for transmitting direct (unmodulated) digital signals through cables

## Slide 70
For the relatively short distances between components on a printed circuit board or along a computer backplane, the amplifiers are in simple IC chips that operate from standard +5v power.
The normal effects are properties of transmission through metallic conductors, and become more pronounced as the conductor length increases. To compensate for distortion, signal power must be increased or the transmission rate decreased. Special amplifier circuits are designed for transmitting direct (unmodulated) digital signals through cables. For the relatively short distances between components on a printed circuit board or along a computer backplane, the amplifiers are in simple IC chips that operate from standard +5v power.

## Slide 71
The normal output voltage from the amplifier for logic '1' is slightly higher than the minimum needed to pass the logic '1' threshold.
Correspondingly for logic '0', it is slightly lower
The difference between the actual output voltage and the threshold value is referred to as the noise margin, and represents the amount of noise voltage that can be added to the signal without creating an error:
tput voltage from the amplifier for logic '1' is slightly higher than the minimum needed to pass the logic '1' threshold

## Slide 72
Correspondingly for logic '0', it is slightly lower
The difference between the actual output voltage and the threshold value is referred to as the noise margin, and represents the amount of noise voltage that can be added to the signal without creating an error:

## Slide 74: Transmission over Medium Distances
Computer peripherals such as a printer or scanner generally include mechanisms that cannot be situated within the computer itself
Our first thought might be just to extend the computer's internal buses with a cable of sufficient length to reach the peripheral
Doing so, however, would expose all bus transactions to external noise and distortion even though only a very small percentage of these transactions concern the distant peripheral to which the bus is connected. If a peripheral can be located within 20 feet of the computer, however, relatively simple electronics may be added to make data transfer through a cable efficient and reliable
To accomplish this, a bus interface circuit is installed in the computer:

## Slide 76
It consists of a holding register for peripheral data, timing and formatting circuitry for external data transmission, and signal amplifiers to boost the signal sufficiently for transmission through a cable
When communication with the peripheral is necessary, data is first deposited in the holding register by the microprocessor.
This data will then be reformatted, sent with error-detecting codes, and transmitted at a relatively slow rate by digital hardware in the bus interface circuit
In addition, the signal power is greatly boosted before transmission through the cable
These steps ensure that the data will not be corrupted by noise or distortion during its passage

## Slide 77
In addition, because only data destined for the peripheral is sent, the party-line transactions taking place on the computer's buses are not unnecessarily exposed to noise. Data sent in this manner may be transmitted in byte-serial format if the cable has eight parallel channels (at least 10 conductors for half-duplex operation), or in bit-serial format if only a single channel is available.

## Slide 78
Efficient data transmission is highly dependent on the characteristics of the transmission medium
correct matching of the selected medium
The transmission medium is the physical path between the transmission and receive
It takes the form of metallic conductors but it can also be achieved through the transmission of a light beam along a glass fiber by means of on electromagnetic beam
It can be don through free space

## Slide 79
These amplifiers are devices that have linear input/output characteristics to reproduce in the output an amplified version of the signal
amplification is very much particular with analogue signals
With digital data Repeaters are required for every 2 or 3 km. For a repeater an incoming signal is amplified and truncated to a fixed level to provide a copy of the input pulse.

## Slide 80: CABLING
The wires in twisted pair cabling are twisted together in pairs
Each pair consists of a wire used for the +ve data signal and a wire used for the -ve data signal
Any noise that appears on 1 wire of the pair will also occur on the other wire.
the wires are opposite polarities, they are 180 degrees out of phase (180 degrees - phasor definition of opposite polarity)
When the noise appears on both wires, it cancels or nulls itself out at the receiving end
Twisted pair cables are most effectively used in systems that use a balanced line method of transmission
polar line coding (Manchester Encoding) as opposed to unipolar line coding (TTL logic

## Slide 81: Unshielded Twisted Pair

## Slide 82
The degree of reduction in noise interference is determined specifically by the number of turns per foot
Increasing the number of turns per foot reduces the noise interference
To further improve noise rejection, a foil or wire braid "shield" is woven around the twisted pairs. This shield can be woven around individual pairs or around a multi-pair conductor (several pairs)

## Slide 83: Shielded Twisted Pair

## Slide 84
Cables with a shield are called shielded twisted pair and are commonly abbreviated STP
Cables without a shield are called unshielded twisted pair or UTP.
Twisting the wires together results in characteristic impedance for the cable.
Typical impedance for UTP is 100 ohm for Ethernet 10BaseT cable
UTP or unshielded twisted pair cable is used on Ethernet 10BaseT and can also be used with Token Ring.
It uses the RJ line of connectors (RJ45, RJ11, etc..)

## Slide 85
STP or shielded twisted pair is used with the traditional Token Ring cabling or ICS - IBM Cabling System
It requires a custom connector. IBM STP (shielded twisted pair) has a characteristic impedance

## Slide 86: Coaxial Cable
Coaxial cable consists of two conductors
The inner conductor is held inside an insulator with the other conductor woven around it providing a shield
An insulating protective coating called a jacket covers the outer conductor

## Slide 87: Optical fiber
Optical fiber consists of thin glass fibers that can carry information at frequencies in the visible light spectrum and beyond
The typical optical fiber consists of a very narrow strand of glass called the core
Around the core is a concentric layer of glass called the cladding. A typical core diameter is 62.5 microns (1 micron = 10-6 meters)
Typically Cladding has a diameter of 125 microns Coating the cladding is a protective coating consisting of plastic, it is called the Jacket

## Slide 88: OPTICAL FIBRE

## Slide 89
An important characteristic of fiber optics is refraction. Refraction is the characteristic of a material to either pass or reflect light
When light passes through a medium, it "bends" as it passes from one medium to the other
An example of this is when we look into a pond of water

## Slide 91
If the angle of incidence is small, the light rays are reflected and do not pass into the water
If the angle of incident is great, light passes through the media but is bent or refracted

## Slide 92: TRANSMISSION IN OPTICAL FIBRE

## Slide 93
Optical fibers work on the principle that the core refracts the light and the cladding reflects the light
The core refracts the light and guides the light along its path
The cladding reflects any light back into the core and stops light from escaping through it - it bounds the medium

## Slide 94: Optical Transmission Modes
There are three primary types of transmission modes using optical fiber. They are
Step Index
Graded Index
Single Mode
Step index has a large core, so the light rays tend to bounce around inside the core, reflecting off the cladding.
This causes some rays to take a longer or shorter path through the core.
Some take the direct path with hardly any reflections while others bounce back and forth taking a longer path
The result is that the light rays arrive at the receiver at different times. The signal becomes longer than the original signal
LED light sources are used. Typical Core: 62.5 microns

## Slide 96: Step Index Mode
Graded index has a gradual change in the core's refractive index
This causes the light rays to be gradually bent back into the core path
This is represented by a curved reflective path in the attached drawing
The result is a better receive signal than with step index. LED light sources are used. Typical Core: 62.5 microns

## Slide 98: Graded Index Mode
Both step index and graded index allow more than one light source to be used (different colors simultaneously), so multiple channels of data can be run at the same time!
Single mode has separate distinct refractive indexes for the cladding and core
The light ray passes through the core with relatively few reflections off the cladding
Single mode is used for a single source of light (one color) operation. It requires a laser and the core is very small: 9 microns.

## Slide 100: Comparison of Optical Fibers

## Slide 101
We don't use frequency to talk about speed any more, we use wavelengths instead
The wavelength of light sources is measured in nanometers or 1 billionth of a meter
Indoor cable specifications:
LED (Light Emitting Diode) light source
3.5 dB/Km Attenuation (loses 3.5 dB of signal per kilometer)
850 nM - wavelength of light source
Typically 62.5/125 (core dia/cladding dia)
Multimode - can run many light sources.

## Slide 102: Outdoor cable specifications
Laser Light Source
1 dB/Km Attenuation (loses 1 dB of signal per kilometer)
1170 nM - wavelength of light source
Monomode (single mode)
Laser Light Source
1 dB/Km Attenuation (loses 1 dB of signal per kilometer)
1170 nM - wavelength of light source
Monomode (single mode)

## Slide 103: Advantages of Optical Fiber:
Noise immunity: RFI and EMI immune (RFI - Radio Frequency Interference, EMI -Electromagnetic Interference)
Security: cannot tap into cable.
Large Capacity due to BW (bandwidth)
No corrosion
Longer distances than copper wire
Smaller and lighter than copper wire
Lower attenuation over long distances
Negligible crosstalk
Faster transmission rate

## Slide 104: Disadvantages of optical fiber:
Physical vibration will show up as signal noise!
Limited physical arc of cable
Bend it too much and it will break
Difficult to splice
The cost of optical fiber is a trade-off between capacity and cost
At higher transmission capacity, it is cheaper than copper
At lower transmission capacity, it is more expensive.

## Slide 105: Transmission Media - Unguided
Unguided transmission media is data signals that flow through the air
They are not guided or bound to a channel to follow
They are classified by the type of wave propagation

## Slide 106: RADIO TRANSMISSION
Data is also propagated using radio in free space termed software medium for example the use of line – of – sight microware radio transmission.
These are applied to over come situations where cable can not easily be laid, such as to link buildings on advancement sites separated by a public road
Such terrestrial links are subjected to electrical and atmospheric disturbance, a disadvantage which is not present in satellite transmission where the radio beam travels most of its path through free space

## Slide 107
Terrestrial microware system for long-haul telecommunications are used as an alterative to coaxial cable or fiber optic links
As with coaxial cable systems, the microware link can support high data rates over long distances The important parameters for radio transmission is the design of the transmitting system and the carrier frequencies involved
At UHF frequencies the radiation system consists of a parabolic dish which is highly directional

## Slide 108
Directivity is related to the ratio of the dish diameter D, and the wavelength and is usually eats as gain G; G = ( D / A ) d B
The range ,d , between communicating line-of-sight parabolic aerials with no intervening obstacles is given by d = 7. 14 (kh)1/2 km. where h, is the aerial height (km ) and k is a factor to take into account the curvature the Earth (approve =1 . 33)

## Slide 109: SATELITE COMMUNICATION
A communication satellite is in effect, a microware relay station.
It is used as a device for point to point and broadcast transmission (ie it operator as a broadcast medium ) stations can transmit to the satellite and a satellite transmission can be received by many stations.
The satellite receives a transmission on a frequency band known as the uplink frequency and retransmits down to the ground also known as the frequencies used should be ideally between 1 and 10 GHz
attenuation by atmospheric absorption is greater above 10 GHz
higher frequencies than this are being used due to the situation of the ideal band range

## Slide 110: Problems affecting sateliate transmission
These are chiefly the high cost of placing the satelite correctly in or bit and high power level required in order to relay information back to Earth station, which will need to be equipped with high gain dish aerials .
the lengthy transmission path will result in a considerable transmission signal delay of about 240 – 300 ms .
This is noticeable in ordinary telephone conversation and can introduce problem in digital data transmission.
Recently there has been significant interest in the development of low Earth Orbiting Satellite ( LEO ) for commercial communication systems. Such systems consists of a number of satellites each operating in of circular orbit at heights of between 50 – 1600 km,
Under these conditions launching cost is low, transmission delay is reduced and power requirements minimized.
A major difficulty is a shift in carrier frequency that occur due to Doppler shift as the satellites gasses over a receiving station.
transmission waveform 1s and 0s

## Slide 111: RF Propagation
There are three types of RF (radio frequency) propagation:
Ground Wave
Ionospheric
Line of Sight (LOS)
Ground wave propagation follows the curvature of the Earth
Ground waves have carrier frequencies up to 2 MHz. Amplitude Modulation (AM) radio is an example of ground wave propagation

## Slide 113
Ionospheric propagation bounces off of the Earth's ionospheric layer in the upper atmosphere.
It is sometimes called double hop propagation. It operates in the frequency range of 30 - 85 MHz. Because it depends on the Earth's ionosphere, it changes with the weather and time of day
The signal bounces off of the ionosphere and back to earth
AM radios operate in this range

## Slide 115
Line of sight propagation transmits exactly in the line of sight
The receiving station must be in the view of the transmit station
It is sometimes called space waves or tropospheric propagation
It is limited by the curvature of the Earth for ground-based stations (100 km, from horizon to horizon). Reflected waves can cause problems
Examples of line of sight propagation are: Frequency modulation (FM) radio, microwave and satellite.

## Slide 117: Radio Frequencies
Name Frequency (Hertz) Examples
Gamma Rays 1019+
X-Rays 1017
Ultra-Violet Light 7.5 x 1015
Visible Light 4.3 x 1014
Infrared Light 3 x 1011

## Slide 118: Radio Frequencies cont.
EHF - Extremely High Frequencies 30 GHz (Giga = 109) Radar
SHF - Super High Frequencies 3 GHz Satellite & Microwaves
UHF - Ultra High Frequencies 300 MHz (Mega = 106) UHF TV (Ch. 14-83)
VHF - Very High Frequencies 30 MHz FM & TV (Ch2 - 13)
HF - High Frequencies 3 MHz2 Short Wave Radio
MF - Medium Frequencies 300 kHz (kilo = 103) AM Radio
LF - Low Frequencies 30 kHz Navigation
VLF - Very Low Frequencies 3 kHz Submarine Communications
VF - Voice Frequencies 300 Hz Audio
ELF - Extremely Low Frequencies 30 Hz Power Transmission

## Slide 119
Radio frequencies are in the range of 300 kHz to 10 GHz.
We are seeing an emerging technology called wireless LANs.
Some use radio frequencies to connect the workstations together, some use infrared technology.
.

## Slide 120: Microwave
Microwave transmission is line of sight transmission. The transmit station must be in visible contact with the receive station.
This sets a limit on the distance between stations depending on the local geography.
The line of sight due to the Earth's curvature is only 50 km to the horizon.
Repeater stations must be placed so that the data signal can hop, skip and jump across the country.
Microwaves operate at high operating frequencies of 3 to 10 GHz.
This allows them to carry large quantities of data due to their large bandwidth.
Microwaves operate at high operating frequencies of 3 to 10 GHz. This allows them to carry large quantities of data due to their large bandwidth.

## Slide 122: Advantages
They require no right of way acquisition between towers.
They can carry high quantities of information due to their high operating frequencies.
Low cost land purchase: each tower occupies only a small area.
High frequency/short wavelength signals require small antennae.
Disadvantages:
Attenuation by solid objects: birds, rain, snow and fog and buildings.
Reflected from flat surfaces like water and metal.
Diffracted (split) around solid objects.
Refracted by atmosphere, thus causing beam to be projected away from receiver

## Slide 123: Disadvantages
Attenuation by solid objects: birds, rain, snow and fog and buildings.
Reflected from flat surfaces like water and metal.
Diffracted (split) around solid objects.
Refracted by atmosphere, thus causing beam to be projected away from receiver.

## Slide 124: Satellite
Satellites are transponders (units that receive on one frequency and retransmit on another) that are set in geostationary orbits directly over the equator.
These geostationary orbits are 36,000 km from the Earth's surface. At this point, the gravitational pull of the Earth and the centrifugal force of Earth's rotation are balanced and cancel each other out.
Centrifugal force is the rotational force placed on the satellite that wants to fling it out into space.
The uplink is the transmitter of data to the satellite.
The downlink is the receiver of data. Uplinks and downlinks are also called Earth stations because they are located on the Earth.
The footprint is the "shadow" that the satellite can transmit to, the shadow being the area that can receive the satellite's transmitted signal.

## Slide 127
The uplink is the transmitter of data to the satellite
The downlink is the receiver of data. Uplinks and downlinks are also called Earth stations because they are located on the Earth
The footprint is the "shadow" that the satellite can transmit to, the shadow being the area that can receive the satellite's transmitted signal.

## Slide 128
Iridium Telecom System
The Iridium Telecom System is a new satellite system that will be the largest private aerospace project.
It is a mobile telecom system intended to compete with cellular phones.
It relies on satellites in lower Earth orbit (LEO). The satellites will orbit at an altitude of 900 - 10,000 km in a polar, non-stationary orbit.
Sixty-six satellites are planned.
The user's handset will require less power and will be cheaper than cellular phones.
There will be 100% coverage of the Earth.

## Slide 130: TRANSMISSION IMPAIRMENT
A number of transmission limitations set a fundamental limit to the rate at which data can be transmitted through a medium and the accuracy with which it can be reconstituted. These are, (i) Attenuation (ii) Distortion (iii) Nose (iv) Bandwidth

## Slide 131: Attenuation
For hardware media the signal attenuation is generally logarithmic and expressed as a constant number of decibels per unit distance. The attenuation of a software media is proportional to the square of the distance from the transmitter but for terrestrial transmission this can also be affected by atmospheric conditions.
The installation of linear amplifiers (for analogue signals) or repeaters (for digital signals) at intervals along the transmission path operates to counter the effects of signal attenuation.
It does this by restoring the signal to a level sufficiently above the accompanying noise level to permit the signal to be received without error.
Attenuation in a given medium is a function of frequency so that different spectral constituents of a signal behave differently with distance from the transmitter.

## Slide 132: DISTORTION
Frequency distortion can be quite severe with analogue (and hence carrier) systems. Equalization techniques such as loading coils and filters are commonly introduced into line transmission systems to minimize these effects, but can lead to deletion of results with digital transmission due to transient impulse signals initiated by the leading edge of the rectangular waveform.

## Slide 133: Delay distortion
Delay distortion can also be introduced by hardware media propagation and its caused by the variation of the frequency of the velocity of propagation through the medium
Delay distortion is particularly serious with data transmission where it causes the spectra associated with one digit pulses to affect the spectral adjacent pulses
This is known as inter-symbol interference

## Slide 134: NOISE
The four general recognized categories of noise in data transmission are –
(1)Thermal noise
(2) Gaussian noise
(3) Jitter noise
(4) Impulse noise.
Carrier systems are also subject to inter-modulation noise which occurs when signals of deferent frequencies share the same transmission medium and encounter some non-linearity in the system, eg a non-linear amplifier.
Adjacent metallic conductors can be affected by cross – talk due to electrical coupling existing between neighboring transmission lines

## Slide 135: THERMAL NOISE
Thermal noise is due to thermal agitation of elections in a conductor.
It has a uniformly wide spectrum and is a function of temperature.
Although is it cannot be eliminated and represents an upper bound on communications system performance,
its actual level is very small (about 100 db selective to 1 mw for a bandwidth in tens of MHz region)
It can be ignored for most applications.

## Slide 136: GAUSSIAN NOISE
Gaussian noise occurs in any transmission system which contains amplifiers.
In the PSTN (public switch telephone network ) Gaussian noise can be heard as background hiss)
This noise has a zero direct current (dc) value and has an approximately Gaussian amplitude distribution.
For a given noise threshold level there is some particular probability that the noise will add to the value of the signal and change a correct signal into an incorrect one.

## Slide 137: IMPULISE NOISE
This consists of angular pulses or pulse bursts, such as radiated ignition interference from automobiles .
The interfering pulses are often high amplitude, and although of limited duration
they can encompass very many consecutive bits of data and can irreparably damage a transmission frame .
In such a situation the damage frame would be detected and a request forwarded for its retransmission

## Slide 138: SIGNAL – TO – NOISE RATIO
The parameter used for determining the noise performance of a transmission is its signal to noise (SNR ) ratio .
Let the signal power be S, and the noise by N the signal – to – noise radio is S / N and the quantity is expressed in decibels as
SNK = (10 log 10 Signal Power/ Noise Power) db
This determines the possible data rate in a given situation

## Slide 139: JITTER – NOISE
The continuous series of short- term departures of the individual transmitted pulses from their correct time position is known as phase jitter.
When isolated from the affected pulses, phase jitter shares many of the characteristics electrical noise and can be regarded as a phase shift noise additive to the signal.
A major source of jitter noise lies in the process of digital regeneration within repeaters spaced at intervals along a transmission medium.
This depends on the pattern content of the transmitted signal and its often termed pattern dependent jitter.

## Slide 140
The root-mean- square ( r. m. s ) value depends on the number of repeaters N through which the signal passes, the bandwidth B, of the timing recovery event and the low – frequency power density of jitter injected at each repeater P. Hence the r. m. s value becomes.
r. m. s jitter = ((PNB)/2 ) ½ for N > 100
This error or increases or accumulated with each passage through a repeater

## Slide 141: The public switched telephone Network
The public switched telephone Network(PSTN), speech or other analogue signals constituting a communication channel on the PSTN, is only conveyed as far as the local switching exchange in its original 300 – 400 Hz bandwidth form.
At the exchange it is joined by many other channels which are then combined together for onward transmission (switching) over a single wide band communication channel
The process of modulation evolves the variation of some parameter of one signal, the carrier with the message signal

## Slide 142
The modulated carrier can then be transmitted to its destination and an inverse process of demodulation invokes to recover the original modulation signal message.
The advantage of using a carrier system in the PSTN instead of transmitting the speech signal directly is that the speech are no longer limited to sharing a spectral location within the same low frequency region.
Types of modulation techniques includes Amplitude modulation, Multiplexing, Frequency modulation. Phase modulation and Pulse code modulation

## Slide 143: MODEM CATEGORIES
the modem enables digital data to be represented by an analogue carrier signal,
With increasing transmission speed come greater complexity. In terms of speed of operation, modulation methods are categorized based on speed.
Low speed ( up to 300 bps ) using FSK ( frequency – shift keying )
Medium opened ( up to 1200 bps ) using Differentiated Phase Shift Keying (DPSK )
High speed ( 2400 bps or more ) using, QA (Quadrate amplitudes modulation)

## Slide 144: DATA RATIOS
Data rates for telegraphy and data carried on the telephone system have data rates related to 75 x 2n eg 75, 150, 300, - …9600.
These rates have nothing, in common with computer network transmission rates, which are based on a multiple or sub multiple of digital transmission rate ,64 k bps ( ISDN ) Integrated Service Digital Network ) Error – Connection modes .
Two Techniques are used in modem designed to overcome data errors due to noise .
(1) Automatic Repeat Request (ARQ) flow control and Error correction scheme.

## Slide 145
The general principle is to hold the outgoing data in a buffer register until an acknowledgement or request for retransmission is made,
this ensures that the undistorted data is not lost before it is checked at the receiving end.
In general, modems convert analogue signals from PSNT lines to digital signals so that it can be transmitted and the modem at the destination convert it back to analogue such that it can be received by the destination PSTN device.

## Slide 146
Forward error correction of asynchronous data is employed in fast modems operating at 9600 to 19200 bps) in which additional bits are added to the data being transmitted

## Slide 147: BASEBAND MODEMS
A part from modulation / demodulation system, a number of devices are available which perform similar function but operate directly on the digital input signal
These are referred to as baseband modems or line drivers and carry out data transmission without modulating or demodulating a carrier signal.
The digital signal is first filtered to reduce the high frequency content and the modified signal is transmitted directly over the line media.
Baseband modems are only suitable for transmission over short distances but can achieve data rates up 192 kbps.

## Slide 148: THE CODEC
the codec ( coder / decoder ) allow analogue data to be represented by digital signals. (transmission and storing speech information in digital from over data network
The analogue signal is subjected to an analogue / digital conversion process to approximate the signal to an equivalent bit stream
At the receiving end the bit stream is used to reconstitute the analogue signal

## Slide 149
digital data transmitted often contains strings of repeated characters which can result in spectral peaks in the transmission information which can cause interference with adjacent channels
To overcome this, codec randomizes the data by scrambling the bit stream (i .e re-ordering of the message digits for transmission)
This is carried out by adding the signal being transmitted to the sum of certain selected stage outputs from multi- stage shift register to which the signal input is applied ( A reverse process is carried out at the same time.

## Slide 150: THE MODERN MODEM
The modern modem does more than simply, converting digitally coded information into a form suitable for transmission over a telephone network
The modem is designed for duplex operation, that is the simultaneous transmission of data in both directions over two-wire telephone circuits.
The most common method for bit speeds of up to 1200 bps;
(1) is simple frequency division multiplexing which the full telephone bandwidth is employed for both directions of transmission,

## Slide 151
(2) adaptive canceling circuits used in each receiver to cancel the interference from both its own transmission and returned echoes.
The modem contains other electronics such as equalization filters to minimize channel distortion, automatic answering facilities, data compression / expansion, automatic channel speed recognition and bit rate switching (so called frequency ‘agiles’ modems ) and facsimile equipment connection
All these are in the modem as a result of a microprocessor fixed in the modem

## Slide 152: MULTIPLEXING
Establishing connections with a large number of terminals or devices requires multiple channels
These need to be transmitted as a group as costs of communications are to be kept low
A solution is to use multiplexing techniques either in the form of a compute network, which is considered as a form of distributed multiplier sharing communication time or bandwidth between connected devices
or hardware multiplexing unit or a concentrator to combine the data traffic from a number of devices into a single stream for transmission over the medium.

## Slide 153: MULTIPLEXING cont’
A multiplexer attempts to maintain data transparency, in the sense that the data input is identical in form to the data output although it will be combined with other data from other channels
A concentrator, on the other hand can operate on the data as well thus carrying out some data processing on the signals to removal of blank spaces included in the input data, thus applying a form of code compression to the message
thus reduces the transmission bandwidth requirement - the removed spaces can be replaced by carrying out code expansion at the receiving end.

## Slide 154: GROOMING
In this process a number of channels carrying mixed signals are grouped
mixture of digital packet such as samples for speech, video or data transmission are processed within the device to produce an output stream of each signal
which contains packets of only one medium’s type of signal.

## Slide 155: Consolidation
It is synonymous with concentration in which a number of input channels convey sequential packets of data interspersed with empty packets to where no information is carried
The consolidation acts to remove redundant packets in each channel and assemble the valid data from all input channels as a single data stream
This long data will need to include details of where input signal with empty packets are removed together with the identification of each channel or permit re-assembly of the combined data

## Slide 156: FREQUNCY DIVISION MULTIPLEXING (FDM)
The use of frequency division multiplexing ( FDM ) is to share the circuit capacity of a single transmission line
It is a type of multiplexing in which the available signal bandwidth is divided into separate sections with each section used for one channel of communication

## Slide 157: TIME DIVISION MULTIPLEXING(TDM)
In Time division multiplexing ( TDM) the time available transmission is subdivided into separate time slots with each slot for one channel of communication
It is used to provide high density transmission
e.g Time slots in radio and TV transmission

## Slide 158: CODE DIVISION MULTIPLEXING (CDM)
This is an encrypted method originally developed for the military in order to overcome interference or jamming.
The technique involves multiplying the data signal to be coded with a high bit rate; pseudo – random code
To recover the data this unique code needs to be known at the receiving end to be multiplied to the transmission signal

## Slide 159: BROADBAND TRANSMISSION
frequency division multiplexing ( FDM ) enables the share of circuit capacity of a single transmission line
When broadband systems are used for data transmission a separate modem operating frequency is required for each channel, and this frequency needs to be different for each direction of transmission
Thus the modems in this mode(broadband modems) form a complementary pair

## Slide 160: BROADBAND TRANSMISSION cont’
This means the transmitting channel used by one modem becomes the receiving channel of the other and vice versa
There are two solution to this problem;
The first is to employ frequency – a gile modems
These modems are able to change operating frequency in response to a signal sent from a central controlling device or a computer

## Slide 161: BROADBAND TRANSMISSION cont
The second is to route all the transmitted signals to a signal device called a HEADENED which counts a whole set of the transmitted frequencies into another set of frequencies used only for reception
The advantage of the technique is that the pair of modems need not be complimentary but can be identical; both transmitting on one frequency and receiving at another

## Slide 162: Baseband Signaling
When a digital data is conveyed directly over the entire capacity of the line used to support the transmission of a single 0 or 1 bit at a time, it is referred to as a baseband signaling
its applied when only one digital signal is transmitted as in point-to-point connection or a TDM situation where the time available for transmission of a number of signals is share the link
At any given time only one digital signal element can be present on the transmission line
This is a problems associated to baseband signaling

## Slide 163: Baseband Signaling conti’
First only one derive connected to the line can transmit at a time
other wise the transmitted data will be corrupted
Secondly, it is necessary to know precisely the type and duration of each digit transmitted so that the logical value can be recognized at the receiving end
In the case of TDM, the channel allocation for each of the transmitted digits must be known

## Slide 164: Baseband Signaling conti’
It implies that means must be found to recognize when two or move devices attempt to transmit at the same time
How to deal with the consequences should this occur
This is a difficulty with broadcast media in each Local Area Network as transmissions fail (Complex methods are recalled to overcome this)

## Slide 165: Synchronous Time – division Multiplexing
With both forms of TDM each channel is allocated the full digital bandwidth of the communication link in turn
Giving to each terminal user the impression of realizing a fraction of the total bandwidth, but allocated permanently
This gives rise to a difficulty that a time-slot allocated is made repeatedly for a given channel whether this does or does not have data to transmit at the time of allocation

## Slide 166: Synchronous Time – division Multiplexing
Due to the dialogue or busty nature of much computer generated data; this can result in idle channel with consequent waste of available bandwidth

## Slide 167: Statistical Time Division Multiplexing
The statistical TDM or ‘statmix’ is used to overcomes this. From the graphs. We can see that us the stat TDM or stratum eg channels 1, 2, 4, 7, 9, and 12 are narrow and could represent each containing a single flag bit permitting other channels e g 3, 5,6, to be excluded for

## Slide 168: Choice Of Multiplexing Technique
TDM can be used to interleave bits or characters from various channels being multiplexed
Bit – interleave multiplexers are used with or synchronous data source.
Each time slot contains just one bit
They are fast in operation since very little delay is experienced, are suitable for medium -to – high speed devices such as synchronous VDUs termials
A single bit buffer is included in each incoming data circuit
Character device operating under start – stop control require a character – interleaved multiplexer.

## Slide 169: Choice Of Multiplexing Technique
With synchronous T D M Input Channels one allocating a time slot to each channel in strict rotation
if all the channel operate at the same speed then there is to need to identify a permissible channel since they all follow in a recognized sequence
It is however necessary to maintain overall synchronization between a transmitter and a receiver since if a transmitter or a receiver are out of step, then data is lost.
To achieve this data is organized into frames with a synchronizing digit added

## Slide 170: Modulation Techniques
Modulation techniques are methods that are used to encode digital information in an analog world. The 3 basic modulation techniques are as follows:
AM (amplitude modulation)
FM (frequency modulation)
PM (phase modulation)
All 3 modulation techniques employ a carrier signal
A carrier signal is a single frequency that is used to carry the intelligence (data).
For digital, the intelligence is either a 1 or 0.
When we modulate the carrier, we are changing its characteristics to correspond to either a 1 or 0

## Slide 171: Modulation Techniques conti’
Modulation techniques are methods that are used to encode digital information in an analog world. The 3 basic modulation techniques are as follows:
AM (amplitude modulation)
FM (frequency modulation)
PM (phase modulation)
All 3 modulation techniques employ a carrier signal. A carrier signal is a single frequency that is used to carry the intelligence (data). For digital, the intelligence is either a 1 or 0. When we modulate the carrier, we are changing its characteristics to correspond to either a 1 or 0.

## Slide 172: Amplitude Modulation- AM
Amplitude Modulation modifies the amplitude of the carrier to represent 1s or 0s
In the above example, a 1 is represented by the presence of the carrier for a predefined period of 3 cycles of carrier. Absence--or no carrier--indicates a 0.
Advantages:
Simple to design
Disadvantages:
Noise spikes on transmission medium interfere with the carrier signal
Loss of connection is read as 0s

## Slide 173: Frequency Modulation- FM
Frequency Modulation modifies the frequency of the carrier to represent the 1s or 0s.
In the above example, a 0 is represented by the original carrier frequency, and a 1 by a much higher frequency (the cycles are spaced closer together).
Advantages:
Immunity to noise on transmission medium
Always a signal present
Loss of signal easily detected
Disadvantages:
Requires 2 frequencies
Detection circuit needs to recognize both frequencies when signal is lost

## Slide 174: PM - Phase Modulation
Phase Modulation modifies the phase of the carrier to represent a 1 or 0
The carrier phase is switched at every occurrence of a 1 bit, but remains unaffected for a 0 bit
The phase of the signal is measured relative to the phase of the preceding bit
The bits are timed to coincide with a specific number of carrier cycles (3 in this example = 1 bit).
Advantage:
Only 1 frequency used
Easy to detect loss of carrier
Disadvantages:
Complex circuitry that is required to generate and detect phase changes.

## Slide 175: Modem Modulation
Here are the 3 basic types of modulation used in modems:
FSK - Frequency Shifted Keying
QPSK - Quadrature Phase Shift Keying
QAM - Quadrature Amplitude Modulation
Modern modems use a combination of the above basic modulation techniques and compression to achieve high data transfer rates (14.4 Kbps and up)

## Slide 176: FSK - Frequency Shift Keying
Frequency Shift Keying (or FSK) is the frequency modulation of a carrier that represents digital intelligence
For Simplex or Half Duplex operation, a single carrier (1170 Hz) is used - communication can only be transmitted in one direction at a time
A Mark or 1 is represented by 1270 Hz, and a Space or 0 is represented by 1070 Hz
The following diagram shows the Voice Channel with Simplex/Half Duplex FSK.
Simplex / Half Duplex FSK

## Slide 177: Full Duplex FSK
For Full Duplex (i.e. simultaneous data communication in both directions), the upper bandwidth of the Voice Channel is utilized
Another carrier is added at 2125 Hz
A Mark or 1 is represented by 2225 Hz, and a Space or 0 is represented by 2025 Hz
The originating modem (the one which dials the phone number and starts the connection) uses the lower carrier (1170 Hz) and the answer modem (the one which answers the ringing phone line) uses the upper carrier (2125 Hz)
This allocation of carriers is done automatically by the modem's hardware
The following diagram shows the Voice Channel with Full Duplex FSK

## Slide 178: Full Duplex FSK conti’
The originate modem transmits on the 1170 Hz carrier and receives on the 2125 Hz carrier
The answer modem receives on the 1170 Hz carrier and transmits on the 2125 Hz carrier
This way, both modems can be transmitting and receiving simultaneously
The FSK modem described above is used for 300 baud modems only.
The logical question is: "Why not use it for higher modems?"
Higher data rates require more bandwidth

## Slide 179
This would require that the Mark and Space frequencies for each band be moved farther apart (the originate and answer bands become wider)
The two carriers would have to move farther apart from each other to prevent crosstalk (interference with each other)
The limit for present phone lines is 1200 Baud Half Duplex (one way) used by Bell 202 compatible modems

## Slide 180: Quadrature Phase Shift Keying
28b. QPSK - Quadrature Phase Shift Keying
Quadrature Phase Shift Keying employs shifting the phase of the carrier at a 600 baud rate plus an encoding technique
QPSK is used in Bell 212A-compatible modems and V.22 - both are 1200 bps Full Duplex standards
The originate modem transmits at 1200 Hz, and receives on 2400 Hz
The answer modem receives on 1200 Hz, and transmits on 2400 Hz
The digital information is encoded using 4 (Quad) level differential PSK at 600 baud.

## Slide 181: FRAME
A frame consists of a group of binary digits generally in additional bits.
Transmission consists sending a sequence of consecutive frames across the network which can be individually checked at the receiving end
Basic modulation methods in modem design is assisted by incorporation of a number of ancillary tasks, including multiplexing
Multiplexing of a number of channels into one transmission routs is achieved by frequency Division multiplexing ( F D M )or time division multiplexing ( T D M )
The F D M is used in the Public Switch Telephone Network ( P S T N )
While the (T D M ) is applied to data transmission, viable length data frames are used in the statistical method which is shown to be more economical in use of available bandwidth than fixed length multiplexing

## Slide 182: Data on the Telephone network
The circuit used to translates digital information into a form suited to voice transmission is known as a modulator and the circuit to perform the reverse function is known as a demodulator
Transmission is normally a duplex ( in both directions ) as both circuits are required at each end
The combination is called a modem ( modulator / demodulator )
Two other modes of operation are in use
These are half duplex mode where both ends of the communication link can send and receive information but not at the same time
In simplex mode information can only be sent in one direction across the link
Early modems were exorcise and limited in performance to a low transmission rate of 300 dps full duplex or 1200 dps ( half duplex over a normal PSTN

## Slide 183: Data Switching
Data Switching is the transmission of data in any kind of essentially transfixing or switching the data from one node in the network to the next in the passage from the originating station attached to a node to the intended receiving station associated with different node.

## Slide 184: CIRCUIT Switching in PSTN
In such a service distinct phases of operation can be distinguished namely
(1) Call mediation by lifting the receiver and dialing
(2) conversation exchange
(3) Termination of the call by replacing the handset
There are 3 processes involves ;
Circuit establishment - the settling up of an end – to –end circuit through an appropriate set of nodes located between the two end devices on the network, i e establishing a dedicated route .
Data transfer- transmission of data across the network following the dedicated route
Circuit disconnect- termination of the connection after data transfer is completed and the separate node paths made available for other data signal.

## Slide 185: CIRCUIT Switching in PSTN conti’
The essential feature of circuit switching lies in the existence of a dedicated communication path between the two end devices
circuit establishment demands a certain amount of elapsed time ( set – up – time ) before a message can be sent.
To do this a cell request signal needs to be sent and this requires an acknowledgement
Each node needs time to set up the route of its onward connection through the network
e g the set up time for the PSTN is relatively ( tens of seconds) but with a computer – controlled exchange this need to be reduced to a few tens of milliseconds

## Slide 186: CIRCUIT Switching in PSTN conti’
End device A, requires a connection to end device B ( A might be for eg microprocessor and B a printer )
First it is necessary to establish the complete circuit between A and B where data can flow
to do this A sends a request to its connecting node for onward connection to B
stored in the node software will be details of routes available and the order of preference based on economy of use and dynamic consideration such as channels availability
We will assume that node 3 forms the next part of the route 4, 6, or 4, 6, 3 can also be chosen)
A dedicated channel is allocated between nodes 1 and 3 and similar request is made at node 3 in which all onward routes are considered except that leading back to node 1.

## Slide 187: CIRCUIT Switching in PSTN conti’
assuming node 5 is selected it remains for this request access to its connected device B
if this is ready to accept data then an acknowledgement is passed through the dedicated route to device A and the process of data transfer commences
(normally the allocated connection between A and B will almost certainly be duplex )

## Slide 188: CIRCUIT Switching in PSTN conti’
For very short interaction it comes or significant overhand up the connections which caucused be tolerate in bank or cash traction or accrete booking inf channel capacity is allocated for the duration of the requires connection even if little or no data is belling transferred it is easeful is PSTN and private exchange which may varying speech darts, fancied and other services in digitally seceded

## Slide 189: MESSAGE SWITCHING
It is not necessary to establish is advance a dedicated path between two end devices. Instead if a device wishes to send a message it appends a destination address to the message data to be delivered to the end device ( or devices ) to which the message is to the be delivered.
This message is then passed through the network from node to node over a traversed route . At each nodes the entire message is stored briefly and transmitted to the next node the process is repeated until the message has reached its destination . This process is termed store – and forward technique.
Advantages over Circuit Switching
It does not require a dedicated channel or data route set up procedure but the entire message must be received at each node so that it can be transmitted ie total transmission delay is variable and generally longer than with Circuit Switching .

## Slide 190: PACKET SWITCHING
In packet – switching the message handle much smaller data lengths than are found in message switching. The message is to be transmitted is divided into a series data called data packets having a maximum length of only a few thousand bits.
Advantages The short packet experiences minimum delay in progression through a high performance network.
The method used is still a store and - forward process but since the packets are small they are quickly transmitted by each node and require little memory space. Secondly by appending a sequences number to each packet as it move to its destination address the nodes are able to interleave packets from several different sources. This leads to more efficient use of the transmission mode ( P S was first applied to ARPANET AND TRNUST)

## Slide 191: THE DATAGRAM
In the datagram approach, each packet is treated independently. As it routes distances across a series of nodes to its destination can vary depending on the network traffic.
Datagrams are single packet messages each of which contains the full addresses of the destination in its header also require ie sequence number so that its place in a sequence can be determined

## Slide 192
Example of a datagram Canadian DATA pac systems.
The network offers a call – base service with two types of calls permanent and switched.
Permanent calls are analogous to a private telephone line and require no call set – up or call clearing
switched calls are analogous to designate calls and packets are classified as normal or prioritized with the latter given preference for onward transmission .

## Slide 193: The Virtual Circuit
In the virtual circuit approach, the logical connection across the network is established between the packet to be sent sent ie a specific data routes or series of nodes are determined so that the packet may be transmitted to reach the end device.
A packet is still stored temporarily at each node and queued for onward transmission together with other packets
Access to the data is obtained using a set of numbers
A virtual circuit is referred to as permanent if it is a leased line or personal.
If the virtual connection can be transferred only to the device the message is intended to, it is termed a virtual call ( eg phoning from a public phone ) and this is connected by means of a call request packet.

## Slide 194
This call request packet must contain both the called end number ( or address ) and the number of a free local logical channel . In the call request, the network routes it to the node connected to the end device called
If this device is free to receive the call the node inserts the number of a logical channel which can carry the incoming data and forwards the call request as an incoming call packet. The end device then retains a call accept packet, which is routed back to the Network connected to the sending device .
This node thus sends a call connects packet to the source node and the establishment of the virtual call is completed.

## Slide 195
Propagation delay - This is the time taken to transmit the data across the media.
Node delay - It is the time taken by the node to carry out the switching process.
Transmission delay -Is the time required for a sending device to transmit data across the network. This depends on the length of the message and the pace of the transmission the network.

## Slide 196
Control for data flowing thro a NW is vested as the used which are generally intelligent microprocessor ie device in and stoned py / data
( i ) Knotting ( ii ) Flowing ( iii) Enron Control

## Slide 197: ROUTING
Routing is one of the most important features in a network that needs to connect with other networks. On this page I will explain the difference between Routed and Routing protocols and explain different methods used to achieve the routing of protocols. The fact is that if routing of protocols was not possible, then we wouldn't be able to communicate using computers because there would be no way of getting the data across to the other end !

## Slide 198
Definition
Routing is used for taking a packet (data) from one device and sending it through the network to another device on a different network. If your network has no routers then you are not routing. Routers route traffic to all the networks in your internetwork. To be able to route packets, a router must know the following

## Slide 199
Destination address
Neighbor routers from which it can learn about remote networks
Possible routes to all remote networks
The best route to each remote network
How to maintain and verify routing information

## Slide 200
Before we go on, I would like to define 3 networking terms :
Convergence: The process required for all routers in an internetwork to update their routing tables and create a consistent view of the network, using the best possible paths. No user data is passed during convergence.
Default Route: A "standard" route entry in a routing table which is used as a first option. Any packets sent by a device will be sent first to the default route. If that fails, it will try alternative routes.
Static Route: A permanent route entered manually into a routing table. This route will remain in the table, even if the link goes down. It can only be erased manually.
Dynamic Route: A route entry which is dynamically (automatically) updated as changes to the network occur. Dynamic routes are basically the opposite to static routes.

## Slide 201
Routers are very common today in every network area, this is mainly because every network these days connect to some other network, whether it's the Internet or some other remote site. Routers get their name from what they do.... which is route data from one network to another.
For example, if you had a company which had an office in Sydney and another one in Melbourne, then to connect the two you would use a leased line to which you would connect a router at each end. Any traffic which needs to travel from one site to another will be routed via the routers, while all the other unnecessary traffic is filtered (blocked), thus saving you valuable bandwidth and money.
There are two type of routers: 1) Hardware routers 2) Software routers.
So what's the difference ?
When people talk about routers, they usually don't use the terms "hardware" or "software" router but we are, for the purpose of distinguishing between the two.

## Slide 202
Hardware routers are small boxes which run special software created by their vendors to give them the routing capability and the only thing they do is simply route data from one network to another. Most companies prefer hardware routers because they are faster and more reliable, even though their cost is considerably more when compared with a software router.
So what does a hardware router look like? Check the picture below, it displays a Cisco 1600 and 2500 series router along with a Netgear RT338 router. They look like a small box and run special software as we said.

## Slide 203
Software routers do the same job with the above hardware routers (route data), but they don't come in small flashy boxes. A software router could be an NT server, NetWare server or Linux server. All network servers have built-in routing capabilities.
Most people use them for Internet gateways and firewalls but there is one big difference between the hardware and software routers. You cannot (in most cases) simply replace the hardware router with a software router.
Why? Simply because the hardware router has the necessary hardware built-in to allow it to connect to the special WAN link (frame relay, ISDN, ATM etc), where your software router (e.g a NT server) would have a few network cards one of which connects to the LAN and the other goes to the WAN via the hardware router.

## Slide 204: IP Routing Process
Example:
In our example, we have 2 networks, Network A and Network B. Both networks are connected via a router (Router A) which has 2 interfaces: E0 and E1. These interfaces are just like the interface on your network card (RJ-45), but built into the router.
Now, we are going to describe step by step what happens when Host A (Network A) wants to communicate with Host B (Network B) which is on a different network.
1) Host A opens a command prompt and enters >Ping 200.200.200.5.

## Slide 205
2) IP works with the Address Resolution Protocol (ARP) to determine which network this packet is destined for by looking at the IP address and the subnet mask of the Host A. Since this is a request for a remote host, which means it is not destined to be sent to a host on the local network, the packet must be sent to the router (the gateway for Network A) so that it can be routed to the correct remote network (which is Network B).
The difficulties and realizable efficiency in routing data through a network depend on the layout and the topology of the network eg if the node

## Slide 206
3) Now, for Host A to send the packet to the router, it needs to know the hardware address of the router's interface which is connected to its network (Network A), in case you didn't realize, we are talking about the MAC (Media Access Control) address of interface E0. To get the hardware address, Host A looks in its ARP cache - a memory location where these MAC addresses are stored for a few seconds .
4) If it doesn't find it in there it means that either a long time has passed since it last contacted the router or it simply hasn't resolved the IP address of the router (192.168.0.1) to a hardware address (MAC). So it then sends an ARP broadcast. This broadcast contains the following "What is the hardware (MAC) address for IP 192.168.0.1 ? ". The router identifies that IP address as its own and must answer, so it sends back to Host A a reply, giving it the MAC address of its E0 interface. This is also one of the reasons why sometimes the first "ping" will timeout. Because it takes some time for an ARP to be sent and the requested machine to respond with its MAC address, by the time all that happens, the TTL (Time To Live) of the first ping packet has expired, so it times out !

## Slide 207
5) The router responds with the hardware address of its E0 interface, to which the 192.168.0.1 IP is bound. Host A now has everything it needs in order to transmit a packet out on the local network to the router. Now, the Network Layer hands down to the Datalink Layer the packet it generated with the ping (ICMP echo request), along with the hardware address of the router. This packet includes the source and destination IP address as well as the ICMP echo request which was specified in the Network Layer.
6) The Datalink Layer of Host A creates a frame, which encapsulates the packet with the information needed to transmit on the local network. This includes the source and destination hardware address (MAC) and the type field which specifies the Network Layer protocol e.g IPv4 (that's the IP version we use), ARP. At the end of the frame, in the FCS portion of the frame, the Datalink Layer will stick a Cyclic Redundancy Check (CRC) to make sure the receiving machine (the router) can figure out if the frame it received has been corrupted. To learn more on how the frame is created, visit the Data Encapsulation - Decapsulation.
7) The Datalink Layer of Host A hands the frame to the Physical layer which encodes the 1s and 0s into a digital signal and transmits this out on the local physical network.

## Slide 208
8)The signal is picked up by the router's E0 interface and reads the frame. It will first do a CRC check and compare it with the CRC value Host A added to this frame, to make sure the frame is not corrupt.
9)After that, the destination hardware address (MAC) of the received frame is checked. Since this will be a match, the type field in the frame will be checked to see what the router should do
with the data packet. IP is in the type field, and the router hands the packet to the IP protocol running on the router. The frame is stripped and the original packet that was generated by Host A is now in the router's buffer.

## Slide 209
10) IP looks at the packet's destination IP address to determine if the packet is for the router. Since the destination IP address is 200.200.200.5, the router determines from the routing table that 200.200.200.0 is a directly connected network on interface E1.
11) The router places the packet in the buffer of interface E1. The router needs to create a frame to send the packet to the destination host. First, the router looks in the ARP cache to determine whether the hardware address has already been resolved from a prior communication. If it is not in the ARP cache, the router sends an ARP broadcast out E1 to find the hardware address of 200.200.200.5

## Slide 210
12) Host B responds with the hardware address of its network interface card with an ARP reply. The router's E1 interface now has everything it needs to send the packet to the final destination.
13)The frame generated from the router's E1 interface has the source hardware address of E1 interface and the hardware destination address of Host B's network interface card. However, the most important thing here is that even though the frame's source and destination hardware address changed at every interface of the router it was sent to and from, the IP source and destination addresses never changed. The packet was never modified at all, only the frame changed.

## Slide 211
14) Host B receives the frame and runs a CRC. If that checks out, it discards the frame and hands the packet to IP. IP will then check the destination IP address. Since the IP destination address matches the IP configuration of Host B, it looks in the protocol field of the packet to determine the purpose of the packet.
15) Since the packet is an ICMP echo request, Host B generates a new ICMP echo-reply packet with a source IP address of Host B and a destination IP address of Host A. The process starts all over again, except that it goes in the opposite direction. However, the hardware address of each device along the path is already known, so each device only needs to look in its ARP cache to determine the hardware (MAC) address of each interface.
And that just about covers our routing analysis. If you found it confusing, take a break and come back later on and give it another shot. Its really simple once you grasp the concept of routing.

## Slide 212: Routed Protocols
Introduction
We all understand that TCP/IP, IPX-SPX are protocols which are used in a Local Area Network (LAN) so computers can communicate between with each other and with other computers on the Internet.
Chances are that in your LAN you are most probably running TCP/IP. This protocol is what we call a "routed" protocol. The term "routed" refers to something which can be passed on from one place (network) to another. In the example of TCP/IP, this is when you construct a data packet and send it across to another computer on the Internet
This ability to use TCP/IP to send data across networks and the Internet is the main reason it's so popular and dominant. If you're thinking also of NetBeui and IPx/SPX,

## Slide 213
then note that NetBeui is not a routed protocol, but IPX/SPX is! The reason for this is actually in the information a packet holds when it uses one of the protocols.
explaination:
If you looked at a TCP/IP or IPX/SPX packet, you will notice that they both contain a "network" layer. For TCP/IP, this translates to the IP layer (Layer 3), as for IPX/SPX, it's the IPX layer (Layer 3). To make it easy to understand, I will use TCP/IP as an example.

## Slide 214
NetBeui on the other hand has no such information! This means that NetBeui has no information about the destination network to which it needs to send the data, as it was developed for LAN use only, or you could say that all hosts are considered to be on the same logical network and all resources are considered to be local. This classifies NetBeui as a "non
Routing protocols were created for routers. These protocols have been designed to allow the exchange of routing tables, or known networks, between routers. There are a lot of different routing protocols, each one designed for specific network sizes, so I am not going to be able to mention and analyse them all, but I will focus on the most popular.

## Slide 215: The two main types of routing: Static routing and Dynamic routing
The router learns about remote networks from neighbor routers or from an administrator. The router then builds a routing table, the creation of which I will explain in detail, that describes how to find the remote networks. If the network is directly connected then the router already knows how to get to the network. If the networks are not attached, the router must learn how to get to the remote network with either static routing (administrator manually enters the routes in the router's table) or dynamic routing (happens automatically using routing protocols).
The routers then update each other about all the networks they know. If a change occurs e.g a router goes down, the dynamic routing protocols automatically inform all routers about the change. If static routing is used, then the administrator has to update all changes into all routers and therefore no routing protocol is used.
Only Dynamic routing uses routing protocols, which enable routers to:
Dynamically discover and maintain routes
Calculate routes
Distribute routing updates to other routers
Reach agreement with other routers about the network topology
Statically programmed routers are unable to discover routes, or send routing information to other routers. They send data over routes defined by the network Administrator.

## Slide 216
A Stub network is so called because it is a dead end in the network. There is only one route in and one route out and, because of this, they can be reached using static routing, thus saving valuable bandwidth.

## Slide 217: Dynamic Routing Protocols
There are 3 types of Dynamic routing protocols, these differ mainly in the way that they discover and make calculations about routes.
1) Distance Vector
2) Link State
3) Hybrid
Distance Vector routers compute the best path from information passed to them from neighbors
Link State routers each have a copy of the entire network map
Link State routers compute best routes from this local map

## Slide 218: Dynamic Routing Protocol
You can also classify the routing protocols in terms of their location on a network
E.g, routing protocols can exist in, or between, autonomous systems
Exterior Gateway Protocols (EGP's) are found between autonomous systems, whereas Interior Gateway Protocols (IGP'S) are found within autonomous systems:
Example of an EGP is the Border Gateway Protocol (BGP) which is also used amongst the Internet routers, whereas examples of IGP protocols are RIP, IGRP, EIGRP

## Slide 219: Distance Vector Protocol
Distance Vector routing protocols use frequent broadcasts (255.255.255.255 or FF:FF:FF:FF) of their entire routing table every 30 sec. on all their interfaces in order to communicate with their neighbors.
The bigger the routing tables, the more broadcasts. This methodology limits significantly the size of network on which Distance Vector can be used.
Routing Information Protocol (RIP) and Interior Gateway Routing Protocol (IGRP) are two very popular Distance Vector routing protocols

## Slide 220: Distance Vector Protocol conti’
Distance Vector protocols view networks in terms of adjacent routers and hop counts, which also happens to be the metric used
The "hop" count (max of 15 for RIP, 16 is deemed unreachable and 255 for IGMP), will increase by one every time the packet transits through a router
So the router makes decisions about the way a packet will travel, based on the amount of hops it takes to reach the destination and if it had 2 different ways to get there, it will simply send it via the shortest path, regardless of the connection speed
This is known as pinhole congestion.

## Slide 221: Distance Vector Protocol conti
Now, when a router is powered on, it will immediately know about the networks to which each interface is directly connected
In this case Router B knows that interface E0 is connected to the 192.168.0.0 network and the S0 interface is connected to the 192.168.10.0 network .routing table required

## Slide 222: Distance Vector Protocol conti
Looking again at the routing table for Router B, the numbers you see on the right hand side of the interfaces are the "hop counts" which, as mentioned, is the metric that distance vector protocols use to keep track on how far away a particular network is
Since these 2 networks are connected directly to the router's interface, they will have a value of zero (0) in the router's table entry
The same rule applies for every router in our example
Remember we have "just turn the routers on", so the network is now converging and that means that there is no data being passed.
When I say "no data" I mean data from any computer or server that might be on any of the networks.

## Slide 223: Distance Vector Protocol conti
During this "convergence" time, the only type of data being passed between the routers is that which allows them to populate their routing tables and after that's done, the routers will pass all other types of data between them
That's why a fast convergence time is a big advantage
One of the problems with RIP is that it has a slow convergence time
Each router will broadcast its entire routing table every 30 seconds
Routing based on Distance Vector can cause a lot of problems when links go up and down, this could result in infinite loops and can also de-synchronize the network
Routing loops can occur when every router is not updated close to the same time.
Let's have a look at the problem before we look at the various solutions:

## Slide 224: Distance Vector Protocol conti
When a say, Network 5 fails, Router E knows about it since it's directly connected to it and tells Router D about it on its next update (when it will broadcast its entire routing table)
This will result in Router D stopping routing data to Network 5 through Router E
But as you can see in the above picture, routers A B and C don't know about Network 5 yet, so they keep sending out update information
Router D will eventually send out its update and cause Router B to stop routing to Network 5, but routers A and C are still not updated
To them, it appear that Network 5 is still available through Router B with a metric of 3.

## Slide 225: Distance Vector Protocol conti
Now Router A sends its regular broadcast of its entire routing table which includes reachability for Network 5
Routers C and B receive the wonderful news that Network 5 can be reached from Router A, so they send out the information that Network 5 is now available
From now on, any packet with a destination of Network 5 will go to Router A then to Router B and from there back to Router A (remember that Router B got the good news that Network 5 is available via Router A).
So this is where things get a bit messy and you have that wonderful loop, where data just gets passed around from one router to another
Seems like they are playing ping pong :)
To deal with these problems we use the following techniques:

## Slide 226: Maximum Hop Count
The routing loop we just described at is called "counting to infinity" and it is caused by gossip and wrong information being communicated between the routers
Without something to protect against this type of a loop, the hop count will keep on increasing each time the packet goes through a router !
One way of solving this problem is to define a maximum hop count
Distance Vector (RIP) permits a hop count of up to 15, so anything that needs 16 hops is unreachable
So if a loop occurred, it would go around the network until the packet reached a hop count of 15 and the next router would simply discard the packet.

## Slide 227: Split Horizon
Split Horizon works on the principle that it's never useful to send information about a router back to the destination from which the original packet came from
So if for example I told you a joke, it's pointless you telling me that joke again !
In our example it would have prevented Router A from sending the updated information it received from Router B back to Router B

## Slide 228: Route Poisoning
Alternative to split horizon, when a router receives information about a route from a particular network, the router advertises the route back to that network with the metric of 16, indicating that the destination is unreachable.
In our example, this means that when Network 5 goes down, Router E initiates router poisoning by entering a table entry for Network 5 as 16, which basically means it's unreachable
This way, Router D is not susceptible to any incorrect updates about the route to Network 5

## Slide 229: Route Poisoning
When Router D receives a router poisoning from Router E, it sends an update called a poison reverse, back to Router E
This make sure all routes on the segment have received the poisoned route information
Route poisoning, used with hold-downs (see section below) will certainly speed up convergence time because the neighboring routers don't have to wait 30 seconds before advertising the poisoned route

## Slide 230: Hold-Down Timers
Routers keep an entry for the network-down state, allowing time for other routers to re-compute for this topology change, this way, allowing time for either the downed router to come back or the network to stabilize somewhat before changing to the next best route is the hold-down time
When a router receives an update from a neighbor indicating that a previously accessible network is not working and is inaccessible, the hold-down timer will start
If a new update arrives from a neighbor with a better metric than the original network entry, the hold-down is removed and data is passed
But an update is received from a neighbor router before the hold-down timer expires and it has a lower metric than the previous route, therefore the update is ignored and the hold-down timer keeps ticking

## Slide 231: Hold-Down Timers
This allows more time for the network to converge
Hold-down timers use triggered updates, which reset the hold-down timer, to alert the neighbor's routers of a change in the network. Unlike update messages from neighbor routers, triggered updates create a new routing table that is sent immediately to neighbor routers because a change was detected in the network.

## Slide 232: Hold-Down Timers
There are three instances when triggered updates will reset the hold-down timer:
1) The hold-down timer expires
2) The router received a processing task proportional to the number of links in the internetwork.
3) Another update is received indicating the network status has changed.
In our example, any update received by Router B from Router A, would not be accepted until the hold-down timer expires
This will ensure that Router B will not receive a "false" update from any routers that are not aware that Network 5 is unreachable
Router B will then send a update and correct the other routers' tables.

## Slide 233: Link State Routing Protocols
Link State protocols, unlike Distance Vector broadcasts, use multicast.
Multicast is a "broadcast" to a group of hosts, in this case routers (Please see the multicast page for more information)
So if I had 10 router of which 4 where part of a "multicast group" then, when I send out a multicast packet to this group, only these 4 routers will receive the updates, while the rest of them will simply ignore the data
The multicast address is usually 224.0.0.5 & 224.0.0.6, this address is defined by the IGRP (Interior Gateway Routing Protocol).

## Slide 234: Link State Routing Protocols
Link State routing protocols do not view networks in terms of adjacent routers and hop counts, but they build a comprehensive view of the overall network which fully describes the all possible routes along with their costs
Using the SPF (Shortest Path First) algorithm, the router creates a "topological database" which is a hierarchy reflecting the network routers it knows about
It then puts it's self on the top of this hierarchy, and has a complete picture from it's own perspective

## Slide 235: Link State Routing Protocols
When a router using a Link State protocol, such a OSPF (Open Shortest Path First) knows about a change on the network, it will multicast this change instantly, there for flooding the network with this information
The information routers require to build their databases is provided in the form of Link State advertisement packets (LSAP).
Routers do not advertise their entire routing tables, instead each router advertises only its information regarding immediately adjacent routers.

## Slide 236: Comparison of link state protocol and distance vector Protocols
Link State protocols in comparison to Distance Vector protocols have:
Big memory requirements
Shortest path computations require many CPU circles
If network is stable little bandwidth is used; react quickly to topology changes
Announcements cannot be “filtered”. All items in the database must be sent to neighbors
All neighbors must be trusted
Authentication mechanisms can be used to avoid undesired adjacencies
No split horizon techniques are possible

## Slide 237: Problems associated with link state protocol
Even though Link State protocols work more efficiently, problem can arise. Usually problems that occur are the cause of changes in the network topology (links go up-down),
All routers don't get updated immediately because they might be on different line speeds, therefore, routers connected via a fast link will receive these changes faster than the others on a slower link
Different techniques have been developed to deal with these problem and these are :
1) Dampen update frequency
2) Target link-state updates to multicast
3) Use link-state area hierarchy for topology
4) Exchange route summaries at area borders
5) Use Time-stamps Update numbering & counters
6) Manage partitions using a area hierarchy
Please select one of the following Link State routing protocols:
Open Shortest Path First - OSPF

## Slide 238: Hybrid Protocols
Hybrid routing protocols are something in-between Distance Vector and Link State routing protocols.
Please select the Hybrid protocol you want to read about:
Enhanced Interior Gateway Routing Protocol - EIGRP

## Slide 239: HUBS
Here we will talk about hubs and explain how they work. In the next section we will move to switches and how they differ from hubs, how they work and the types of switching methods that are available; we will also compare them
Before we start there are a few definitions which I need to speak about so you can understand the terminology we will be using
Domain: Defined as a geographical area or logical area (in our imagination) where anything in it becomes part of the domain
In computer land, this means that when something happens in this domain (area) every computer that's part of it will see or hear everything that happens in it
Collision Domain: Putting it simple, whenever a collision between two computers occurs, every other computer within the domain will hear and know about the collision
These computers are said to be in the same collision domain. As you're going to see later on, when computers connect together using a hub they become part of the same collision domain. This doesn't happen with switches.

## Slide 240: HUBS conti’
Broadcast Domain: A domain where every broadcast (a broadcast is a frame or data which is sent to every computer) is seen by all computers within the domain
Hubs and switches do not break up broadcast domains. You need a router to achieve this.
There are different devices which can break-up collision domains and broadcast domains and make the network a lot faster and efficient
Switches create separate collision domains but not broadcast domains
Routers create separate broadcast and collision domains.
Hubs are too simple to do either, can't create separate collision or broadcast domain

## Slide 241: Hubs & Repeaters
Hubs and repeaters are basically the same, so we will be using the term "Hub" to keep things simple
Hubs are common today in every network.
They are the cheapest way to connect two or more computers together Hubs are also known as Repeaters and work on the first layer of the OSI model
They are said to work on the first layer because of the function they perform
They don't read the data frames at all (like switches and routers do), they only make sure the frame is repeated out on each port and that's about it

## Slide 242: Hubs & Repeaters
The Nodes that share an Ethernet or Fast Ethernet LAN using the CSMA/CD rules are said to be in the same collision domain
In plain English, this means that all nodes connected to a hub are part of the same collision domain
In a Collision domain, when a collision occurs everyone in that domain/area will hear it and will be affected
The Ethernet section talks about CSMA/CD and collision domains since they are part of the rules under which Ethernet functions.

## Slide 243: The picture below shows a few hubs : 8 port Netgear and a D-link hub.
The computers (nodes) connect to the hub using Unshielded Twisted Pair cable (UTP).
Only one node can be connected to each port of the hub. The pictured hub has a total of 8 ports, which means up to 8 computers can be networked
When hubs were not that common and also expensive, most offices and home networks use to install coax cable
The way hubs work is quite simple and straightforward: When a computer on any one of the eight ports transmits data, this is replicated and sent out to the other seven ports
Check out the below picture which shows it clearly

## Slide 244: Hubs
EXPLANATION:
Node 1 is transmitting some data to Node 6 but all nodes are receiving the data as well. This data will be rejected by the rest of the nodes once they figure out it's not for them
This is accomplished by the node's network card reading the destination MAC address of the frame (data) it receives, it examines it and sees that it doesn't match with it's own and therefore discards the frame
Please see the Datalink layer in the OSI section for more information on MAC addresses
Most hubs these days also have a special port which can function as a normal port or as an "uplink" port

## Slide 245: Hubs
An uplink port allows you to connect another hub to the existing one, increasing the amount of ports which will be available to you
This is a cheap solution when you need to get a few more computers networked and it works quite well up to a point
This is how 2 eight port hubs would look when connected via the uplink port and how the data is replicated to all 16 ports :

## Slide 246: Hubs
In the above picture you can see that Node 1 is again transmitting data to Node 6 and that every other node connected to the hub is receiving the information
As we said, this is a pretty good and cheap solution, but as the network gets busier, you can clearly understand that there is going to be a lot of unnecessary data flowing all over the network
All Nodes here are in the same broasdcast and collision domain since they will hear every broadcast and collision that occurs
This is the same situation you get when you use coax cable, where every node or computer is connected onto the same cable and the data that's put onto it travels along the cable and is received by every computer

## Slide 247: Hubs
Most hubs these days also have a special port which can function as a normal port or as an "uplink" port
An uplink port allows you to connect another hub to the existing one, increasing the amount of ports which will be available to you
This is a cheap solution when you need to get a few more computers networked and it works quite well up to a point
This is how 2 eight port hubs would look when connected via the uplink port and how the data is replicated to all 16 ports :

## Slide 248: Hubs
You probably also noticed the two orange boxes labled "50 Ohm"
These are called terminating resistors and are used on both ends of the coax cable so when the signal gets to them, it's absorbed by them and that way you don't get the signal reflecting back
Think of them as shock absorbent and the data signal is the shock wave which gets absorbed when it reaches the destination
terminating resistors
The coax cable can be up to 185 meters and can contain no more than 30 nodes per segment

## Slide 249: Hubs
What you're looking at in the above picture is one segment 25 meters long with 4 nodes attached to it
Now coming back to the hubs, there are a few standard features most of them have these include a link and activity LED for each port, a power LED and collision LED
Some hubs have separate link lights and activity lights, others combine them into one where the link light will flash when there is activity, otherwise it remains constantly on
The Netgear hub which is displayed at the beginning of this page has two separate LEDs for the activity and link but the Compex hub below has only one.

## Slide 250: Hubs
This little hub also contains a special BNC connection so you can connect a coax cable to it
When you do connect it, the BNC light comes on. Notice the label at the top where they have written "8 port Ethernet Repeater"
As we already have said, hubs are just simple repeaters
The collision light on the hubs will only light up when a collision is detected.

## Slide 251: Hubs
Collision is when 2 computers or nodes try to talk on the network at the same time.
When this happens, their frames will collide and become corrupted. The hubs are smart enough to detect this and will light up the collision LED for a small amount of time (1/10 of a second for each collision)
If you find yourself wondering why couldn't they make things work so more than two computers can talk on the network
Read about Ethernet where all this is explained in detail about;
Collisions and the fact that only one computer can talk on the network at any given time along with the cabling rules are all part of the Ethernet rules. Remember that any node connected to a hub becomes part of the same collision domain

## Slide 252: Switching Technology
As we mentioned earlier, hubs work at the first layer of the OSI model and simply receive and transmit information without examining any of it.
Switches (Layer-2 Switching) are a lot smarter than hubs and operate on the second layer of the OSI model.
What this means is that a switch will not simply receive data and transmit it throughout every port, but it will read the data and find out the packet's destination by checking the MAC address
The destination MAC address is located always at the beginning of the packet so once the switch reads it, it is forwarded to the appropriate port so no other node or computer connected to the switch will see the packet.

## Slide 253: Switching Technology
Switches use Application Specific Integrated Circuits (ASIC's) to build and maintain filter tables
Layer-2 switches are a lot faster than routers because they do not look at the Network Layer ( i.e Layer-3) header or if you like, information
Instead all they look at the frame's hardware address (MAC address) to determine where the frame needs to be forwarded or if it needs to be dropped
If we had to point a few features of switches we would say:

## Slide 254: Switching Technology conti’
They provide hardware based bridging (MAC addresses)
They work at wire speed, therefore have low latency
They come in 3 different types:
Store & Forward, Cut-Through and Fragment Free (Analysed later)
Below is a picture of two typical switches. Notice how they looks similair to a hubs, but they aren't. It's just that the difference is on the inside!

## Slide 255: The Three Stages of switching
All switches regardless of the brand and various enhancements they carry, have something in common, it's the three stages (sometimes 2 stages) they go through when powered up and during operation.
These are as follows:
Address Learning
Forward/Filter decisions
Loop Avoidance (Optional)

## Slide 256: Address Learning
When a switch is powered on, the MAC filtering table is empty
When a device transmits and an interface receives a frame, the switch places the source address in the MAC filtering table remembering the interface on which the device on is located
The switch has no choice but to flood the network with this frame because it has no idea where the destination device is located

## Slide 257: Address Learning conti’
If a device answers and sends a frame back, then the switch will take the source address from that frame and place the MAC address in the database, associating this address with the interface that received the frame.
Since the switch has two MAC addresses in the filtering table, the devices can make a point-to-point connection and the frames will only be forwarded between the two devices.
This makes layer-2 switches better than hubs.
In a hub network all frames are forwarded out to all ports every time.
Most desktop switches these days can hold up to 8000 MAC addresses in their table, and once the table is filled, then starting with the very first MAC entry, the switch will start overwriting the entries.
Even though the number of entries might sound big .. it only takes a minute or two to fill it up, and if a workstation does not talk on the network for that amount of time, then chances are that its MAC address has been removed from the table and the switch will forward to all ports the packet which has a destination for a particular workstation.

## Slide 258: Address Learning conti’
Most desktop switches these days can hold up to 8000 MAC addresses in their table, and once the table is filled, then starting with the very first MAC entry, the switch will start overwriting the entries.

## Slide 259: Address Learning conti’
Even though the number of entries might sound big ,it only takes a minute or two to fill it up, and if a workstation does not talk on the network for that amount of time, then chances are that its MAC address has been removed from the table and the switch will forward to all ports the packet which has a destination for a particular workstation.

## Slide 260: Address Learning conti’
And after the first frame has been successfully received by Node 2, Node 2 sends a reply to Node 1, check out what happens:
Notice how the frame is not transmitted to every node on the switch.
The switch by now has already learned that Node 1 is on the first port, so it send it straight there without delay
From now on, any communication between the two will be a point-to-point connection

## Slide 261: Forward/Filter Decision
When a frame arrives at the switch, the first step is to check the destination hardware address, which is compared to the forward/filter MAC database.
If the destination hardware address is known, then it will transmit it out the correct port, but if the destination hardware address is not known, then it will broadcast the frame out of all ports, except the one which it received it from
If a device (computer) answers to the broadcast, then the MAC address of that device is added to the MAC database of the switch.

## Slide 262: Loop Avoidance
It's always a good idea to have a redundant link between your switches, in case one decides to go for a holiday.
When you setup redundant switches in your network to stop failures, you can create problems.
Have a look at the picture below and I'll explain:
The above picture shows an example of two switches which have been placed in the network to provide redundancy in case one fails.
Both switches have their first port connected to the upper section of the network, while their port 2 is connected to the lower section of the same network.
This way, if Switch A fails, then Switch B takes over, or vice versa.
Things will work fine until a broadcast come along and causes alot of trouble.
For the simplicity of this example, I am not going to show any workstations, but only the server which is going to send a broadcast over the network, and keep in mind that this is what happens in real life if your switch does not support Spanning-Tree Protocol (STP), this is why I stuck the "Optional" near the "Loop Avoidance" at the start of this section:

## Slide 263: Loop Avoidance
The Server for one reason or another decides to do a broadcast. This First Round (check arrow) broadcast is sent down to the network cable and firstly reaches Port 1 on Switch A.
As a result, since Switch A has Port 2 connected to the other side of the lan, it sends the broadcast out to the lower section of the network, this then is sent down the wire and reaches Port 2 on Switch B which will send it out Port 1 and back onto the upper part of the network.

## Slide 264: Loop Avoidance
At this point, as the arrows indicate (orange colour) the Second Round of this broadcast starts.
So again... the broadcast reaches Port 1 of Switch A and goes out Port 2 back down to the lower section of the network and back up via Port 2 of Switch B
After it comes out of Port 1 of Switch B, we get the Third Round, and then the Fourth Round, Fifth Round and keeps on going without stopping.....!
This is what we call a Broadcast Storm

## Slide 265: Loop Avoidance
A Broadcast Storm will repeat constantly, chewing up the valuable bandwidth on the network.
This is a major problem, so they had to solve it one way or another, and they did... with the Spanning-Tree Protocol or STP in short
What STP does, is to find the redundant links, which this case would be Port 2 of Switch B and shut it down, thus eliminating the possibility of looping to occur.

## Slide 266: LAN Switch Types
At the begining of this page we said that the switches are fast, therefor have low latency. This latency does vary and depends on what type of switching mode the switch is operating at. You might recall seeing these three switching modes at the beginning: Store & Forward, Cut-Through and Fragment Free.
The picture below shows how far the different switching modes check the frame:

## Slide 267: LAN Switch Types
So what does this all mean ? Switching modes ? I Don't understand !
Let's Explain!
The fact is that switches can operate in one of the three modes. Some advance switches will allow you to actually pick the mode you would like it to operate in, while others don't give you any choice. Let's have a quick look at each mode:

## Slide 268: Store & Forward mode
This is one of the most popular switching methods
In this mode, when the switch receives a frame from one of it's ports, it will store it in memory, check it for errors and corruption, and if it passes the test, it will forward the frame out the designated port, otherwise, if it discovers that the frame has errors or is corrupt, it will discard it. This method is the safest, but also has the highest latency.

## Slide 269: Cut-Through (Real Time)
Cut-Through switching is the second most popular method
In this mode, the switch reads the frame until it learns the destination MAC address of the frame it's receiving
Once it learns it, it will forward the frame straight out the designated port without delay
This is why we say it's -Real Time-, there is no delay or error checking done to the frame

## Slide 270: Fragment Free
The Fragment free switching method is mainly used to check for frames which have been subject to a collision.
The frame's first 64 bytes are only checked before forwarding the frame out the designated port.
Reason for this is because almost all collisions will happen within the first 64 bytes of a frame.
If there is corruption in the first 64 bytes, it's most likely that that frame was a victim of a collision
Just keep one important detail in mind:
When you go out to buy a switch, make sure you check the amount of memory it has.

## Slide 271: Fragment Free conti’
A lot of the cheap switches which support the Store &Forward mode have very small amounts of memory buffer (256KB- 512KB) per port.
The result of this is that you get a major decrease in performance when you have more than 2 computers communicating via that switch cause there isn't enough memory to store all incoming packets (this also depends on the switching type your switch supports), and you eventually get packets being discarded
The table below is a guide on what amounts of memory you should be looking at for switches of different configuration

## Slide 272: Bridges
A bridge is device filters data traffic at a network boundary
Bridges reduce the amount of traffic on a LAN by dividing it into two segments
Bridges operate at the data link layer (Layer 2) of the OSI model.
Bridges inspect incoming traffic and decide whether to forward or discard it
An Ethernet bridge, for example, inspects each incoming Ethernet frame - including the source and destination MAC addresses, and sometimes the frame size - in making individual forwarding decisions

## Slide 273: Bridges conti’
Bridges serve a similar function as switches, that also operate at Layer 2
Traditional bridges, though, support one network boundary, whereas switches usually offer four or more hardware ports
Switches are sometimes called "multi-port bridges" for this reason
Bridges tend to be more complex than hubs or repeaters
Bridges can analyze incoming data packets to determine if the bridge is able to send the given packet to another segment of the network.

## Slide 274: Network Bridge
A network bridge connects multiple network segments at the data link layer (layer 2) of the OSI model
The term layer 2 switch is very often used interchangeably with bridge.
Bridges are similar to repeaters or network hubs, devices that connect network segments at the physical layer; however, with bridging, traffic from one network is managed rather than simply rebroadcast to adjacent network segments
In Ethernet networks, the term "bridge" formally means a device that behaves according to the IEEE 802.1D standard—this is most often referred to as a network switch in marketing literature

## Slide 275
Since bridging takes place at the data link layer of the OSI model, a bridge processes the information from each frame of data it receives
In an Ethernet frame, this provides the MAC address of the frame's source and destination
Bridges use two methods to resolve the network segment that a MAC address belongs to-Transparent bridging and Source route bridging

## Slide 276: Transparent bridging
This method uses a forwarding database to send frames across network segments.
The forwarding database is initially empty and entries in the database are built as the bridge receives frames. I
f an address entry is not found in the forwarding database, the frame is rebroadcast to all ports of the bridge, forwarding the frame to all segments except the source address.
By means of these broadcast frames, the destination network will respond and a route will be created along with recording the network segment to which a particular frame is to be sent,

## Slide 277: Transparent bridging conti’
bridges may also record a bandwidth metric to avoid looping when multiple paths are available
Devices that have this transparent bridging functionality are also known as adaptive bridges
They are primarily found in Ethernet networks.

## Slide 278: Source route bridging
With source route bridging two frame types are used in order to find the route to the destination network segment.
Single-Route (SR) frames make up most of the network traffic and have set destinations
while All-Route (AR) frames are used to find routes Bridges send AR frames by broadcasting on all network branches;
Each step of the followed route is registered by the bridge performing it
Each frame has a maximum hop count, which is determined to be greater than the diameter of the network graph, and is decremented by each bridge

## Slide 279: Source route Bridging conti’
Frames are dropped when this hop count reaches zero, to avoid indefinite looping of AR frames.
The first AR frame which reaches its destination is considered to have followed the best route, and the route can be used for subsequent SR frames; the other AR frames are discarded
This method of locating a destination network can allow for indirect load balancing among multiple bridges connecting two networks.
The more a bridge is loaded, the less likely it is to take part in the route finding process for a new destination as it will be slow to forward packets.
A new AR packet will find a different route over a less busy path if one exists.

## Slide 280: Source route Bridging conti’
This method is very different from transparent bridge usage, where redundant bridges will be inactivated
however, more overhead is introduced to find routes, and space is wasted to store them in frames
A switch with a faster backplane can be just as good for performance, if not for fault tolerance. They are primarily found in Token Ring networks

## Slide 281: Advantages of network bridges
Self configuring
Primitive bridges are often inexpensive
Reduce the size of collision domain by microsegmentation in non switched networks
Transparent to protocols above the MAC layer allows the introduction of management/performance information and access control
LANs interconnected are separate, and physical constraints such as number of stations, repeaters and segment length don't apply
Helps minimize bandwidth usage

## Slide 282: Disadvantages of network bridges
Does not limit the scope of broadcasts
Does not scale to extremely large networks
Buffering introduces store and forward delays; on average traffic destined for bridge will be related to the number of stations on the rest of the LAN
Bridging of different MAC protocols introduces errors
Because bridges do more than repeaters by viewing MAC addresses, the extra processing makes them slower than repeaters
Bridges are more expensive than repeaters

## Slide 283: Disadvantages of network bridges
Although infinite bridges (or layer 2 switches) can be connected in theory, often a broadcast storm will result as more and more collisions occur
Collisions delay service advertisements, which causes the hosts to back off and attempt to retransmit after a pseudo-random interval
Because bridges simply repeat any Layer 2 broadcast traffic, this can result in undesirable

## Slide 284
example would be a bridge in between adjacent office buildings. It is unlikely that the advantages of bridging would outweigh the loss of network bandwidth associated with all of the service advertisements.
Another major disadvantage is that any standards-compliant implementation of bridging cannot have any closed loops in a network. This limits both performance and reliability.

## Slide 285: Bridging versus routing
Bridging and routing are both ways of performing data control, but work through different methods
Bridging takes place at OSI Model Layer 2 (Data-Link Layer) while Routing takes place at the OSI Model Layer 3 (Network Layer)
This difference means that a bridge directs frames according to hardware assigned MAC addresses while a router makes its decisions according to arbitrarily assigned IP Addresses
As a result of this, bridges are not concerned with and are unable to distinguish networks while routers can

## Slide 286: Bridging versus routing
When designing a network, one can choose to put multiple segments into one bridged network or to divide it into different networks interconnected by routers
If a host is physically moved from one network area to another in a routed network, it has to get a new IP address
if this system is moved within a bridged network, it doesn't have to reconfigure anything. These days bridges are replaced with switches

## Slide 287: Bridge versus Layer 2 Switch conti’
Bridge frame handling is controlled in the bridge's software. Conversely, layer 2 switch performs address recognition and frame forwarding with hardware
Similarly, a router and a layer 3 switch differ only by whether they forward in software, or hardware.
A bridge can typically analyze/forward only one packet at a time, while a layer 2 switch has multiple parallel data paths and can handle multiple frames simultaneously.

## Slide 288
A bridge uses store-and-forward (it buffers the incoming frame, and then performs a CRC to ensure data integrity before forwarding the frame)
while a layer 2 switch can be configured to either use store-and-forward, or to use cut-through (sending the frame through as soon as the destination MAC address is realized, without checking the data for correctness).

## Slide 289
Because a layer 2 switch can incorporate the functions of a bridge, the bridge has suffered commercially
New installations typically include layer 2 switches with bridge functionality, rather than bridges.
This has led to the general mixing of the two terms- Brouter

## Slide 290: Wireless bridge conti’
A wireless bridge is a hardware component used to connect two or more network segments (LANs or parts of a LAN) which are physically and logically (by protocol) separated
.It does not necessarily always need to be a hardware device, as some operating systems (such as Windows, Linux, Mac OS X and FreeBSD) provide software to bridge different protocols
This is seen commonly in protocols over wireless to cable. So in a sense the computer acts as a bridge by using bridging O/S software.

## Slide 291: Wireless bridge conti’
wireless routers and wireless access points offer either a "bridge" mode or a "repeater" mode, both of which perform a similar common function.
The difference being the bridge mode connects to different protocol types and the repeater modes relays the same protocol type
Wireless routers, access points, and bridges are available that are compliant with the IEEE802.11a, b, g and n standards
The frequency bands for these wireless standards can be used license-free in most countries

## Slide 292: Wireless bridge CONTI’
Wireless bridge devices work in pairs (point-to-point), one on each side of the "bridge". However, there can be many simultaneous "bridges" using one central device (point to multipoint)
During bridge setup, the wireless devices used for the bridge must be set to the same service set identifier (SSID) and radio channel

## Slide 293: Wireless bridge conti’
Bridging has historically referred to propagation of data across a device without traversing a network stack, such as TCP/IP
Wireless bridging is a colloquial term.
A more accurate description of connecting two local area networks would be a Wireless LAN to LAN bridge
The distinction is important
While device may not support bridging to a remote wireless access point to connect two LANs,
It may be desirable (and supported) that a wireless access point support true bridging; where packets traverse from a wireless to wired network without passing through an internal protocol stack, firewall or other network abstraction.

## Slide 294: Wireless bridge conti
Two bridged networks could be treated as parts of a single subnet under Internet Protocol (IP)
A wireless client would be able to make a DHCP request from a wired server if the wired and wireless networks were bridged
In the ISO OSI model, a device in which packets traverse the network layer is considered a router, a device in which packets traverse the data link layer only is considered a bridge

## Slide 295: Transparent Bridging
Transparent bridging refers to a form of bridging "transparent" to the end systems using it, in the sense that the end systems operate as if the bridge isn't there in the way that matters
bridges segment broadcasts between networks, and only allows specific addresses to pass through the bridge to the other network
It is used primarily in Ethernet networks, where it has been standardized as IEEE 802.1D

## Slide 296: Transparent Bridging
The bridging functions are confined to network bridges which interconnect the network segments.
The active parts of the network must form a tree.
This can be achieved either by physically building the network as a tree or by using bridges that use the spanning tree protocol to build a loop-free network topology by selectively disabling network broadcast addresses.
If one computer on network A sent a broadcast packet (packet with destination mac address FF:FF:FF:FF:FF:FF) to address FF:FF:FF:FF:FF:FF, the bridge would stop this from getting to network B.
Note we have 3 addresses: source address and target address of the packet and the address where we send the packet.

## Slide 297: Transparent Bridging
The mac address FF:FF:FF:FF:FF:FF is the broadcast address for both networks; when a frame is sent to this address, the frame is then resent out on every available port on that specific network segment
This method allows the bridge to only switch frames that have a specific MAC address, that is, one that is not mac FF:FF:FF:FF:FF:FF.
When an address is specified and a frame is sent, the bridge automatically switches the frame to both network segments while noting the source MAC addresses' home segment
This allows the bridge to send frames across the networks, by recording and resolving MAC addresses of devices on each side

## Slide 298: Transparent Bridging cont’
Next, the bridges monitor all frames traveling on the network, noting the frame's source addresses in a table, and then broadcasting the frame with a specific destination (not broadcast) address to the other networks, effectively rebroadcasting it to every device available on every network segment until the specified destination is found
Without broadcast segmentation, the bridge would get caught in an infinite loop.

## Slide 299: Transparent Bridging cont’
Note that both source and destination addresses are used in this algorithm. Source addresses are recorded in entries in the table, while destination addresses are looked up in the table and matched to the proper segment to send the frame to.
As an example, consider two hosts (A and B) and a bridge (C). The bridge has two interfaces, (C1, C2).
A is connected to the C1 and B is connected to the C2. Note the physical connection is A - C - B, since C has two ports.
A sends a frame to (C), and C records the source MAC address into its table
The bridge now has an address for A in its table, so it forwards it to B by broadcasting it to FF:FF:FF:FF:FF:FF, or every address possible
B, having received a packet from A, now transmits a packet in response

## Slide 300: Transparent Bridging cont’
this time, the bridge has A's address in the table, so it records B's address sends it to A's unique MAC address specifically
Two-way communication is now possible between A and B without any further broadcasting.
Note, however, that only the bridge along the direct path between A and B possess table entries for B
If a third host (D), on the same side as A sends a frame to B, the bridge simply records the address source, and broadcasts it to B's segment

## Slide 301: Source route bridging
Source route bridging is used primarily on token ring networks, and is standardized in Section 9 of the IEEE 802.2 standard
The spanning tree protocol is not used, the operation of the network bridges is simpler, and much of the bridging functions are performed by the end systems, particularly the sources, giving rise to its name.

## Slide 302: Source route bridging
A field in the token ring header, the routing information field (RIF), is used to support source-route bridging
Upon sending a packet, a host attaches a RIF to the packet indicating the series of bridges and network segments to be used for delivering the packet to its destination
The bridges merely follow the list given in the RIF - if a given bridge is next in the list, it forwards the packet, otherwise it ignores it.

## Slide 303: Source route bridging
When a host wishes to send a packet to a destination for the first time, it needs to determine an appropriate RIF
A special type of broadcast packet is used, which instructs the network bridges to append their bridge number and network segment number to each packet as it is forwarded
Loops are avoided by requiring each bridge to ignore packets which already contain its bridge number in the RIF field
At the destination, these broadcast packets are modified to be standard unicast packets and returned to the source along the reverse path listed in the RIF

## Slide 304: Source route bridging
Thus, for each route discovery packet broadcast, the source receives back a set of packets, one for each possible path through the network to the destination
It is then up to the source to choose one of these paths (probably the shortest one) for further communications with the destination

## Slide 305: Source routing transparent bridging
Source routing transparent bridging, abbreviated SRT bridging, is a hybrid of source routing and transparent bridging, standardized in Section 9 of the IEEE 802.2 standard.
It allows source routing and transparent bridging to coexist on the same bridged network by using source routing with hosts that support it and transparent bridging otherwise

## Slide 306: Gateway
In telecommunications, the term gateway has the following meaning
In a communications network, a network node equipped for interfacing with another network that uses different protocols.
  A gateway may contain devices such as
  protocol translators,
  impedance matching devices, rate converters,
  fault isolators,
  signal translators as necessary to provide system interoperability. It also requires the establishment of mutually acceptable administrative procedures between both networks.

## Slide 307: Gateway
  A protocol translation/mapping gateway interconnects networks with different network protocol technologies by performing the required protocol conversions.
Loosely, a computer configured to perform the tasks of a gateway. For a specific case, see default gateway
Routers exemplify special cases of gateways.

## Slide 308: Gateway
A gateway is a network point that acts as an entrance to another network
On the Internet, a node or stopping point can be either a gateway node or a host (end-point) node
Both the computers of Internet users and the computers that serve pages to users are host nodes, while the nodes that connect the networks in between are gateways
For example, the computers that control traffic between company networks or the computers used by internet service providers (ISPs) to connect users to the internet are gateway nodes

## Slide 309: Gateway
In the network for an enterprise, a computer server acting as a gateway node is often also acting as a proxy server and a firewall server
A gateway is often associated with both a router, which knows where to direct a given packet of data that arrives at the gateway, and a switch, which furnishes the actual path in and out of the gateway for a given packet.
On an IP network, clients should automatically send IP packets with a destination outside a given subnet mask to a network gateway. A subnet mask defines the IP range of a network

## Slide 310: Gateway conti’
For example, if a network has a base IP address of 192.168.0.0 and has a subnet mask of 255.255.255.0, then any data going to an IP address outside of 192.168.0.X will be sent to that network's gateway
While forwarding an IP packet to another network, the gateway might or might not perform Network Address Translation.
A gateway is an essential feature of most routers, although other devices (such as any PC or server) can function as a gateway.

## Slide 311: Gateway conti’
Most computer operating systems use the terms described above
A computer running Microsoft Windows however describes this standard networking feature as Internet Connection Sharing; which will act as a gateway, offering a connection between the Internet and an internal network. Such a system might also act as a DHCP server. Dynamic Host Configuration Protocol (DHCP)

## Slide 312: Gateway conti’
DHCP is a protocol used by networked devices (clients) to obtain various parameters necessary for the clients to operate in an Internet Protocol (IP) network
By using this protocol, system administration workload greatly decreases, and devices can be added to the network with minimal or no manual configurations.